ECS 1801 / 2801 / 4801 CNCs

for 3 Axes Milling Applications

(aligned to 5.00 SW version)

CONCISE PROGRAMMING MANUAL

CODE: 721P201

OCTOBER 2006 EDITION

BASIC ISSUE

INDEX

Basic Instructions to build a Part Program	1

% - Start of Program	1

Nxx - Block identification number	1

(..) - Comment for machine Operator	1

{..}  or ‘..  -  Comment for Programmer	2

[..]  -  Program Label	2

<INP: ”Prompt”; Rxx;  Nxx /Label [;[Min];[Max]]>  -  Input parametric Data	2

/..  - Optional Operation	2

:N..  -  Operation Phase  definition	2

M0  -  Program Stop	2

M1  -  Conditioned Program Stop	2

M02 or M30  -  End of Program	3

Internal Auxiliary Functions	3

G4 Fxx  -  Suspend the program execution for xx seconds	3

G23 /G24 -  Definition of a machinable volume	3

G25 X.. Y.. Z..  -  Low Working Field Limitation	4

G25  -  Remove low working  Field Limitation	4

G26  X.. Y.. Z..  -  Upper Working Field Limitation	4

G26  -  Remove upper Working Field Limitation	4

G70  -  Set the CNC to work in metric	5

G71  -  Set the CNC to work in inches	5

G90  -  Absolute Programming	5

G91  -  Incremental  Programming	5

G94  -  Spindle Working Modality	5

G95  -  Spindle Working Modality	5

G92 S..  -  Set Spindle Speed Limitation	5

F..  -  Set  Desired Profile Feed	5

External Auxiliary Functions	5

M ..  -  Miscellaneous  Auxiliary Functions	5

M03  -  Spindle Clockwise rotation	5

M04  -  Spindle anti-clockwise rotation	5

M05  -  Spindle Stop	5

M06 Tn  -  Load on the spindle the Tool  “n”	5

M08  -  Coolant Liquid flow on	6

M09  -  Coolant Liquid flow off	6

M10  -  Axes Holding	6

M11  -  Axes Release	6

M13  -  Spindle Clockwise rotation + coolant liquid flow on	6

M14  -  Spindle  anti Clockwise rotation + coolant liquid flow on	6

M17  -  Subprograms end	6

M19  -  Spindle Orientation	6

M40 – M45  -  Speed Gear Change	6

T nnnn  -  Desired Tool	6

S nnnn  -  Set Desired Spindle Speed	6

Instructions for parametric  Programming	6

“R”  -  Real  variables	6

Mathematical Operators	7

Trigonometric Functions	7

Generic Mathematical  Functions	7

Instructions to manage Subprograms and Program flow	7

L<Subprogram name>  -  Call a  Sub-program  (direct mode)	7

L<&Rxx>  -  Indirect mode to call a Sub-program  using an R variable	8

M17 or  <RET>  -  End a Subprogram and return to the main Program	8

N.. <JMP:Nx>  -  Un conditioned  jump to Nx  block	8

N..   <JMP:[XXX]>  -  Un conditioned  jump to  [XXX] Label	8

N.. <JMC: Px ; Nx>  -  Un conditioned  jump to Nx block of Px Part Program	8

N.. < IFF<exp>: Na; Nb; Nc>  -  Conditioned  jump to a block	8

N.. < IFC<exp>: Sub1;  Na; Nb; Nc>  -  Conditioned  jump to a block of a Subprogr.	8

N.. <RPT: Ninit; Nend; Rep.>  -  Repetition of a defined number of instructions	8

Instructions for special functions	8

<TIM:ON> - Reset and Start Timer	8

<TIM:OFF>  -  Stop  Timer	9

G309  -  Exclusion  of Automatic Tool  Changer management	9

G308  -  Restart  Automatic Tool  Changer normal operations	9

<MIR:ON; Axis1; Axis2>  -  Mirroring activation	9

<MIR:OFF; Axis1;… >  -  Mirroring  de activation	9

Instructions to manage  Contouring	10

G60 - Precise Positioning and Machining	10

G64 - Rapid  Positioning and Machining	10

G66 - Precise Positioning and Rapid Machining	10

G67 - Smoothing & Filtering  interpolation Activation	11

<G67: ...> - Smoothing & Filtering interpolation Parameter Definition	11

G68 - Special interpolation Disabling	11

G69 - PH interpolation Activation	12

<G69: ...> - PH interpolation Parameter Definition	12

<SPL: ...> - Spline on line management	13

Instructions for Origin management	14

G59 X.. Y.. Z..  -  Apply an offset  to the active Origin	14

G59  Nxx  X.. Y.. Z..   -  Loading of origin  Nxx	14

G58  X.. Y.. RC..  -  Apply  an offset + a rotation  to the active Origin	14

G58 - Reset  all rot - translations	15

G53 - Forces Absolute Machine Origins	15

Instructions for Tools Radius and Length compensation  management	15

D0 - Tool length compensation suspension	15

G43 -  Set Tool Length  compensation along positive direction	15

G44 -  Set Tool Length  compensation along negative direction	16

<DRA: nn>  -  Profile stock definition	16

<DLN: nn>  -  Profile stock in dept	16

Instructions to load  Tools Parameters from a File	16

G795  -  Starts a Loading tool procedure	16

G797  -  Loads Parameters of a new Tool	16

G798  -  Loads / Modifies  Geometrical  Parameters of a Tool	17

G792  -  Associates a comment  to a  Tool	17

G799  -  Loads  Wear & Life parameters	17

G791  -  Loads   Tool  Configurable Parameters	18

G794  -  Loads / Removes  a  tool to/from the warehouse	18

G793  -  Deletes a Tool	18

Interpolation  and Contouring Plane  definition	19

G16 Axis1 Axis2 Axis3 +/-   -  Free selection of Contouring Plane	19

G17 / G18 / G19  -  Standard  Contouring Plane definition	19

G00 / G0  X.. Y.. Z..  -  Rapid Traverse Interpolation	19

G01 / G1  X.. Y.. Z..  -  Linear interpolation  at programmed Working Feed (F…)	19

G02 / G2  I.. J.. XP2 YP2 - Circular clockwise interpolation at Working Feed into XY Contouring Plane	20

G03 / G3  I.. J.. XP2 YP2  -  Circular   anti-clockwise  interpolation  at Working Feed into XY Contouring Plane	20

G10 Xpole Ypole a.. b..   -  Rapid Traverse movements  using Polar Coordinates	21

G11 Xpole Ypole a.. b.. -  Linear movement at working Feed using Polar Coordinates	21

G12/ G13 I..J..  Xpole Ypole a.. b.. -  Clockwise / Anti-clockwise circular interpolation using Polar Coordinates	21

RA..     -  Insertion of a  Rounding Radius  between two geometrical elements	21

SM..     -  Insertion of a  Chamfer  between two linear  elements	22

Tool Radius Compensation and Profile Attach / Detach	22

G41  -  Tool  Compensation ON  - Working Piece at right  side of the tool	22

G42  -  Tool  Compensation ON  - Working Piece at left side of the tool	22

G40  -  Tool  Radius Compensation OFF	24

G47  -  Tang.  Attach with Tool  Comp. ON  - Work. Piece at right  side of the tool	24

G48  -  Tang. Attach with Tool  Comp. ON  - Working Piece at left side of the tool	25

G46  -  Tangential  Detach reaching  the programmed point with Tool  Comp. OFF	25

<TGR: K; Angle>  -  Programming of Radius and Angle of attach	26

Canned Cycles	26

Generalities on Canned Cycles	26

<CFF=CF Axis>  -  Definition of the Axis along which Canned Cycle will be applied	26

G81  -  Standard  Drilling	27

G81/3  -  3 Layers Drilling	27

G82  -  Drilling with Dwell for chip breaking	27

G83  -  Deep Drilling  with clearing	28

G83/r  -  Deep Drilling with Dwell for chip breaking	28

G84  -  Tapping	28

G85  -  Boring	29

G86  -  Boring with Spindle stop	29

G87  -  Boring with Retraction	29

G89  -  Boring with Dwell	30

G80  -  Cancel Canned Cycles G8x	30

G184  -  Solid Threading	30

G184/r -  Solid Tapping	31

Pocket Milling Macros	31

G88 - Boring of an internal Hole	31

G188 - Cylinder External Milling	31

G185 - Roughing of a Rectangular Pocket with central pre-drilling	32

G186 - Finishing of a Rectangular Pocket	32

G187 - Roughing of a Circular “Bean Shaped” Pocket	33

G189 - Roughing of a Circular Pocket with central pre-drilling	33

G190Finishing of a Circular Pocket	34

G175 - Roughing of a Rectangular Pocket with concentric passes	34

G179 - Roughing of a Circular Pocket with concentric passes	34

G150 - Cancels Macro / Canned Cycles  from G151 to G199	35

L<MILL> - Internal/External Flattening of a Rectangular Area	35

G778 - Emptying  of a generic profile pocket – Without finishing step	35

G779 - Emptying  of a generic profile pocket – With finishing step	35

G777 - Definition of parameters used by macro G778 and G779	35

G701 - Definition of pocket and islands profiles used by macro G778 and G779	35

G722 - Machining of Truncated Conical Surface (Archimedean  Spiral)	37

G728 - Machining of 3D Surfaces obtained connecting two profiles that lie on parallel planes	38

G726 - Definition of   parameters  and  first profile used by the G728 macro	38

G727 - Definition of second profile used by the G728 macro	38

G738 - Machining of 3D Surfaces obtained by a “flat” profile and one or more “section” profiles	40

G736 - Definition of   parameters  and  flat profile used by the G738 macro	40

G737 - Definition of “section” profiles used by the G738 macro	40

Macros repetitions on Lines / Arrays	43

L<FORFLA> - Execution of Canned Cycles / Macros on a Arc of Circle	43

L<FORMAT> - Execution of Canned Cycles / Macros on an Array	44

L<WRITE> - Engraving of a String of Characters	45

Static and Dynamic Matrices	45

Static and Dynamic Matrices  -  Basic concepts	45

Static Matrices        Programming	46

L<TRANS> - Single / Multiple Translation Static Matrix	46

L<ROTX> - Rotation around X axis	47

L<ROTY> - Rotation around Y axis	47

L<ROTZ> - Rotation around Z axis	47

L<ROTXYZ> - Rotation in sequence around XYZ axes	47

L<ROTRAS> - Repetition with Roto-translation Static Matrix	47

L<SCALE> - Change Scale Ratio  Static Matrix	48

Dynamic Matrices Programming	48

L<TRACYIL> - Cylindrical Programming - Dynamic Matrix	48

L<DROTX> - Rotation of the Contouring Plane around  the first DMX Axis	49

L<DROTY> - Rotation of the Contouring Plane around  the second DMX Axis	49

L<DROTX> - Rotation of the Contouring Plane around  the third  DMX Axis	49

L<DROTX> - Multiple rotation of the Contouring Plane around  the DMX Axes	49

Measuring Cycles with Probe	50

Measurement Cycles       General  Considerations	50

Measurement Cycles      General  Parameters & Definitions	50

Measurement Cycle         Preparatory Parameters & Instructions	51

G201 - Single Movement  -  Measurement Cycle	51

G202 - Two Internal  Movements  -  Measurement Cycle	52

G203 - Two External  Movements  -   Measurement Cycle	52

G204 - Four Internal  Movements  -  Measurement Cycle	53

G205 - Four External  Movements  -  Measurement Cycle	53

G206 - Three  Internal  Movements  -  Measurement Cycle	54

G207 - Three External Movements  -  Measurement Cycle	54

G208 - Three External Movements  -  Measurement Cycle	55

G210 - Probe Qualification Cycle	55

G211 - Measurement Cycle with Probe in fixed position	56

G200 - Cancels Measurement Cycle	56

Measurement Cycles -  Results Data Collection	57

Measurement Cycles -  Programming Examples	57

# Basic Instructions to build a Part Program

% - Start of Program

The character % must be inserted as first instruction of the Program. Normally it is written alone. In the same block is however accepted a comment . It forces in the CNC the following initial conditions: Axes moving in Rapid Traverse (G0) . Tool Radius Compensation reset (G40) Axes Feed = 100 mm/min (F100) Spindle programming at constant Speed (G94) Spindle rotation = 100 giri/min (S100) Reset of Length and Radius over stock (DRA = DLN=0) Reset Tool Length compensation (D=0) Precise Positioning and Machining mode (G60) Reset “Floating” mode (G30) Reset special interpolations G62, G67 and G69 (G68) Metric Programming (G71) Absolute Programming (G90) Deactivation off all Static and Dynamic Transformation Array (TCT/DCT :OFF) Reset of all Canned Cycles (G80) Reset of all Measurement Cycles (G200) Reset of all Macro cycles (G100-G150-G250) Reset of spindle speed limitation (G92) Reset of TRANSMIT transformation (G36 ) Reset of Working field limitations (G25/G26) Reset of Mirroring function (MIR:OFF) Activation of the contouring Plane associated to the first two configured axes (if, as usual, X and Y - G17) Activation of origin 1 for all configured axes (G54.01) Reset of all Rot-Translation eventually applied to the origins (G58/G59) Notes: The above list reports the default initial conditions set by ECS. If necessary, all the start up parameters, can be however differently initialized by the Machine Builder.

Nxx - Block identification number

Block (Instruction) identification number. It is mandatory only in some instructions associated to the Flow Program control

(..) - Comment for machine Operator

This message will be displayed on the CNC display.

{..} or ‘.. - Comment for Programmer

The CNC manage this format as a not operative Instructions Examples : { This is a Comment } or ‘ This is a Comment

[..] - Program Label

This instruction is typically used with the conditioned jump instruction (<JMP: [Label]> ) to modify the program flow. Notes : The CNC interprets the label as the first eight characters of the string, or the first characters before “:” Eventual spaces between two characters are disregarded. Examples: Digital Label Label interpreted by the CNC [FRAME2] FRAME2 [OBJECT 6] OBJECT6 [F1:MAINWINDOW] F1

<INP: ”Prompt”; Rxx; Nxx /Label [;[Min];[Max]]> - Input parametric Data

This instruction is a simple way to allow to the machine operator to insert data on a parametric program: Prompt = Message displayed on the screen. Rxx = Variable where will be loaded the data introduced by the machine operator. Nxx/Label = Number of block or Label where the execution of the program will jump in case the operator press [ESC] Min Max = Used to define the accepted input range. Example: <INP: ”Radius [mm]”; R0; N100;10;100>.

/.. - Optional Operation

The character ( /) before an instruction makes it optional. In other words the machine operator can, through the Operator Panel key enable or disable its execution. The optional execution can be also controlled by special LIP instructions: <SKP:ON> Disable optional block execution, <SKP:OFF> Enable optional block execution.

:N.. - Operation Phase definition

This instruction is useful to speed up a Search and Repositioning sequence. It forces the same initial conditions configured through the % character. The instruction :N... must be programmed in a line of the program which does not contain other programming instructions, only comments {....} or ‘…… or (....) are allowed.

M0 - Program Stop

It stops program execution till the machine operator press START to resume execution.

M1 - Conditioned Program Stop

It has the same behaviour of M0 but with the possibility to enabled /disabled the function by the Operator Panel . Key: .The optional stop can be also activated by the following specific LIP instructions: <STP:ON> to activate the optional stop <STP:OFF> to disable the optional stop The instruction M1 is used to impose a STOP during various phases of the program typically during the Part Program setting-up.

M02 or M30 - End of Program

These instructions are inserted at the end of the Program, to indicate to the CNC, that the program is finish. They must be written into a block alone.

# Internal Auxiliary Functions

G4 Fxx - Suspend the program execution for xx seconds

Notes: - The maximum value that can be attributed to F is 719.9 seconds. - It is important to make sure that the F.. instruction is correctly positioned in relation to the G04, for example, while it is correct to program: N... G4 F2.5 to specify an interruption of 2.5 seconds, it is not the same thing to write: N.. F2.5 G04 In this last case in fact the instruction F2.5 is interpreted by the CNC as a feed programming..

G23 /G24 - Definition of a machinable volume

Through G23 and G24 functions it is possible to delimit a 3D portion of the Part Program to be machined. To correctly define the “Machinable Limits” ( sometime defined as “Programming Limits”) it is necessary to respect the following rules: They will be defined by making reference to the active origin; Don’t care if a Static or a Dynamic Transformation Matrix or a G58 rot -translation instruction is active. Any change applied to the reference system will affect accordingly the Programming Limits. In other words, the defined machinable volume is intimately linked to the reference system and moves with it. From an operating point of view, the Programming Limits are managed in the following way: Once detected the point where the profile exit from the Volume Limit, the tool is moved backward to a quote obtained adding to the one of the point a configurable safety delta. Then the tool will move in rapid traverse on the vertical to the Volume Limit re-entering point. From here it will go down towards the point. Consequently, if the safety delta is set to zero, when the point where the profile exit from the Volume Limit has been reached, the tool will not be lifted, but will rather reach (this time at working feed) the Volume Limit re-entering point. While the Programming Limits can be only enabled with the CNC in AUTO mode, they can be defined also in MDI or in JOG modalities. Once they have been defined, they can be enabled or disabled (suspended). Therefore, in they became fully operative, they must have been previously defined and also enabled. Syntax: N.. G23 Xmin Ymin Zmin ‘ Definition of the Bottom Left side corner of the Volume Limit N.. G24 Xmax Ymax Zmax ‘ Definition of the Top Right side corner of the Volume Limit N.. G23 ‘ Activation of last defined Bottom Programming Limits N.. G24 ‘ Activation of last defined Top Programming Limits N…G23 X Y Z ‘ Suspension of the last defined Bottom Programming Limits N.. G24 X Y Z ‘ Suspension of the last defined Top Programming Limits Notes: It is not allowed to program the G23 and G24 functions in the same block. The axes labels must follow the G23 and G24 functions. The Safety delta quote has to be programmed through the synonymous DZS associated to the variable #271. With “%”, “:” and “Reset” the Programming Limits already defined are not changed. With CNC Power OFF they are instead lost. Issuing G23 and G24 the tool length compensation must be active because it identify the vertical axes where the Safety delta quote will be applied. The Programming Limits definition can be also done in a fully guided mode through a specific Data Entry that can be activated pressing, on the main CNC menu (second level), the key: For more details please consult the “MILLING MACHINE Instructions of Use” manual, code 721P392.

G25 X.. Y.. Z.. - Low Working Field Limitation

It reduces the lower limit of the configured working field to the programmed value (X, Y and Z quotes are referred to the absolute machine origin). Note: G25….. instruction cannot be written on the same line containing a G26….. instruction.

G25 - Remove low working Field Limitation

Reset the lower working limit field to the configured values. G25 X resets only the limit value of X axis, G25 Y only of Y axis, G25 Z resets only the limit value of Z axis…etc. G25 alone, forces all axes low limits to the initially configured values.

G26 X.. Y.. Z.. - Upper Working Field Limitation

It reduces the upper limit of the configured working field to the programmed value (X, Y and Z quotes are referred to the absolute machine origin). Note: G26 instruction cannot be written on the same line containing a G25….. instruction. .

G26 - Remove upper Working Field Limitation

Reset the upper working limit field to the configured values. G26 X reset only the limit value of X axis, G26 Y only the Y axis, G26 Z only the limit value of Z axis.G26 alone, forces all axes upper limits to the initially configured values.

G70 - Set the CNC to work in metric

G71 - Set the CNC to work in inches

G90 - Absolute Programming

Set the CNC to assume the programmed axes quotes as absolute values. It is a modal instruction automatically forced at the program beginning by the % instruction.

G91 - Incremental Programming

Set the CNC to assume the programmed axes quotes as incremental values. It is however possible to program in incremental way one or more axes without having to use the G91 instruction. In particular, it is possible to program axes in the same block in absolute mode together with others programmed incrementally. To do this, it is sufficient to add the letter D (delta dimension) in front of the name of the involved axes, for example: N20 X10 DY20 Will move the X axis to quote 10 while the Y axis of 20 mm. Note: Incremental Programming cannot be enabled if Polar programming is active.

G94 - Spindle Working Modality

Set the CNC to assume Feed programmed in mm/min and Speed in rpm.

G95 - Spindle Working Modality

Set the CNC to assume Feed programmed in mm/rotation and Speed in rpm. So in this way the Axes Feed will became function of the Spindle Speed.

G92 S.. - Set Spindle Speed Limitation

Definition of the spindle maximum speed in rpm. S…. defines the set maximum Speed

F.. - Set Desired Profile Feed

It allows to define the desired feed on describing the programmed profile. Feed on X, Y and Z axes is expressed in mm/min in case is active the G94 Spindle Working modality. It is instead expressed in mm/rotation in case the active Spindle Working modality is G95.

# External Auxiliary Functions

M .. - Miscellaneous Auxiliary Functions

Miscellaneous Auxiliary Functions can be defined by the machine Builder into the range from M03 to M199. Typical assignments are:

M03 - Spindle Clockwise rotation

It commands the clockwise rotation of the spindle at the programmed Speed.

M04 - Spindle anti-clockwise rotation

It commands the anti-clockwise rotation of the spindle at the programmed Speed.

M05 - Spindle Stop

It commands the spindle to stop.

M06 Tn - Load on the spindle the Tool “n”

It commands a tool change operation ( making an implicit M05) . In case of Automatic Tool Changer it will active the associated operation. In case of Manual Tool Changer it will issue to the operator a specific message to guide him on changing the requested tool.

M08 - Coolant Liquid flow on

It commands the coolant liquid flow.

M09 - Coolant Liquid flow off

It stops the coolant liquid flow.

M10 - Axes Holding

M11 - Axes Release

M13 - Spindle Clockwise rotation + coolant liquid flow on

It commands the clockwise rotation of the spindle to the programmed Speed and the contemporary coolant liquid Flow (M3 + M8).

M14 - Spindle anti Clockwise rotation + coolant liquid flow on

It commands the anti clockwise rotation of the spindle to the programmed Speed and the contemporary coolant liquid issuing (M4 + M8).

M17 - Subprograms end

Its ends the execution of a subprogram commanding the return to the main program ( same function of <RET> instruction).

M19 - Spindle Orientation

Its commands the orientation of the spindle on a predefined angular position (making an implicit M09 + M05).

M40 – M45 - Speed Gear Change

It commands the selections of the desired spindle gear (it has a meaning only if the Milling machine is equipped of a speed gear change).

T nnnn - Desired Tool

It commands the search of the desired “nnnn” tool.

S nnnn - Set Desired Spindle Speed

It commands the spindle to rotate to the programmed Speed. “nnnn” will be expressed in rpm .

# Instructions for parametric  Programming

“R” - Real variables

For general programming the user can utilize 2000 R variables. From R0 to R999 are retentive type variables (their value is maintained also if the CNC is powered off). From R1050 to R2049 are instead non retentive type variables. Variables from R1000 to R1049 cannot be used (their use is ECS reserved ). An R variable can be used directly (through assignment) in all instructions where the argument is Real (Double floating). Examples: X= R1 Y= R2 Z=R3 I=R7 K=R9 S=R10 F=R12 Or after its conversion into Integer or Long through specific instructions (FTI and FTL) Examples: G<FTI(R0)> M<FTI(R3)> T<FTL(R5)> N<FTL(R7)>

Mathematical Operators

Into a mathematical expression can be used the following operators :

+ Addition

- Subtraction

* Multiplication

/ Division

** Power Elevation

// Rest of Division

= Assignment ( The result of the expression right side is assigned to the left side variable)

Examples: R1 = R2 + 10 + R1 R4 = 133 // 40

Trigonometric Functions

SIN(…) Sinus

Examples : R1 = SIN(..) R2 = SIN(R5) (The result of the operation is always a real number)

COS(…) Co Sinus

Examples : R1 = COS(..) R2 = COS(R5) (The result of the operation is always a real number)

TAN(…) Tangent

Examples : R1 = TAN(..) R2 = TAN(R5) (The result of the operation is always a real number)

ASN(…) Arc Sinus

Examples : R1 = ASN(..) R2 = ASN(R5) (The result of the operation is always a real number)

ACS(…) Arc Co sinus

Examples : R1 = ACS(..) R2 = ACS(R5) (The result of the operation is always a real number)

ATN(…) Arc Tangent

Examples : R1 = ATN(..) R2 = COS(R5) (The result of the operation is always a real number)

Generic Mathematical Functions

FTI (…) Conversion from Real to Integer

Example : R1=1.02 G<FTI(R1)> X120 Z200 ( G1 X120 Z200

FTL (…) Conversion from Real to Integer

Example : R12= 14.6 T<FTL(R12)> M06 ( T14 M6

SQR (…) Square Root

Example : R1=50 R2=80 R3= SQR (R1**2 + R2**2) ( R3= 94,34

ABS(…) Absolute Value

Example : R1=123.4 R2=ABS(R1) ( R2=123

RND (…) Round Value

Example : R2=13.55 R1=RND(R2) ( R1 = 14

# Instructions to manage Subprograms and Program flow

L<Subprogram name> - Call a Sub-program (direct mode)

Examples : L<431286> ‘ The execution jumps to 431286 Subprogram L<SUB1> ‘ The execution jumps to SUB1 Subprogram L<C:\ECS.CNC\PROGRAM\SUB2> ‘The execution jumps to SUB2 Subprogram located into the C:\ECS.CNC\PROGRAM folder

L<&Rxx> - Indirect mode to call a Sub-program using an R variable

Example : R12= 100 L<&R12> the execution jumps to 100 Subprogram

M17 or <RET> - End a Subprogram and return to the main Program

The Sub-program execution end and the flow returns to the Main Program.

N.. <JMP:Nx> - Un conditioned jump to Nx block

The execution jumps to the Nx block of the current Program.

N.. <JMP:[XXX]> - Un conditioned jump to [XXX] Label

The execution jumps to the [XXX] label of the current Program.

N.. <JMC: Px ; Nx> - Un conditioned jump to Nx block of Px Part Program

Example: N200 <JMC: PROG1; N50> the program execution jumps to block N50 of Program PROG1.

N.. < IFF<exp>: Na; Nb; Nc> - Conditioned jump to a block

If the result of expression exp is lower than 0 the program flow jumps to Na block. If the result of expression exp is equal to 0 the program flow jumps to Nb block. If the result of expression exp is bigger than 0 the program flow jumps to Nc block. Where Na, Nb and Nc can be also defined as N <exp>. Example: N100 <IFF<R10 - 100>:N50;N150;N200> the program execution is conditioned by the result f the expression R10-100

N.. < IFC<exp>: Sub1; Na; Nb; Nc> - Conditioned jump to a block of a Subprogr.

If the result of expression exp is lower than 0 the program flow jumps to Na block of Subprogram Sub1. If the result of expression exp is equal to 0 the program flow jumps to Nb block of Subprogram Sub1. If the result of expression exp is bigger than 0 the program flow jumps to Nc block of Subprogram Sub1. Where Na, Nb and Nc can be also defined as N <exp>. Example: N100 <IFC<R11 – R12>: S1; N50;N150;N200> the program execution jumps to Subprogram S1 to a block conditioned by the result f the expression R11- R12

N.. <RPT: Ninit; Nend; Rep.> - Repetition of a defined number of instructions

The portion of program limited by instructions Ninit and Nend will be repeated Rep time. If the parameter Rep is omitted the block of instruction is repeated only one time. If the parameter Rep is omitted and the Nend forced equal to the number of the <REP:..> block the sequence of instruction is indefinitely repeated. Examples: N100 <RPT: N100; N200; 3 > the instructions inside the blocks N100 and N200 are repeated three times. N100 <RPT:N80;N100> the instructions inside the blocks N80 to N100 area indefinitely repeated. Note: Inside a Repetition Loop, so between the Ninit and the Nend blocks, other <RPT:...> can be nested (it is however important never exceed the maximum nesting levels that is 7).

# Instructions for special functions

<TIM:ON> - Reset and Start Timer

This instruction reset the internal counter (Variable V1025) and starts to increment it every second

<TIM:OFF> - Stop Timer

This instruction stop the increment of the internal timer V1025. Using <TIM:ON> and <TIM:OFF> instruction is possible the evaluate the execution time of a working process. Example: N100 <TIM:ON> ...... ... Portion of Program of which we want to evaluate the working time ..... N200 <TIM:OFF> N201 R0=V1025 ‘ The variable V1025 contains the elapsed time expressed in sec

G309 - Exclusion of Automatic Tool Changer management

With the G309 command, in case of mechanical fault of the Automatic Tool Changer, it can be momentary disabled and managed as a Manual one.

G308 - Restart Automatic Tool Changer normal operations

Important! The effects of the commands G308 and G309 aren’t loosed powering off the CNC.

<MIR:ON; Axis1; Axis2> - Mirroring activation

Axis1 and Axis2 represent the axes Labels respect which the mirroring will be activated. Examples: <MIR:ON;X> Mirroring active referred only to X axis. <MIR:ON;Y> Mirroring active referred only to Y axis. <MIR:ON;X;Y> Mirroring active referred to both axes X and Y.

<MIR:OFF; Axis1;… > - Mirroring de activation

In case no Axis are specified the Mirroring function will be completely de activated. The character %, at the program beginning, forces a mirroring de activation.

# Instructions to manage  Contouring

G60 - Precise Positioning and Machining

G64 - Rapid Positioning and Machining

G66 - Precise Positioning and Rapid Machining

The main differences between the Contouring Modalities : G60, G64 and G66 are: - A different “Verification of the Limit Curve”; - A different management of the positioning process in terms of “Threshold” to be reached and how long it is maintained. The positioning threshold, expressed in micron, it can be different for every axes. It is set through the “SGL” parameter located into the AXS.TAR configuration file. How long all axes have to stay inside the configured threshold is instead defined through the “CSGL” parameter, expressed Tau (the CNC elementary tick), and located inside the GEN.TAR configuration file. With “Verification of the Limit Curve” we intend the reduction of the feed on the profile corner that the CNC automatically operates in base to the angle associated to the corner itself. This feed reduction, with the exception of G60 modality where the applied rules are a little more complex, is done in an on/off mode in base to a defined angular threshold (identified as AG64 and AG66) . So under these values the corner Feed is the one computed with reference to the acceleration of the involved axes, over these values the movement is instead stopped. In case of G60 are instead defined two different threshold angles (ANGI and ANGF). For angles smaller or equal to ANGI the computed feed isn’t reduced. For angles bigger or equal to ANGF the movement is stopped. For angles between the two thresholds, the computed feed is instead reduced respecting a proportional linear law. The following table synthesize the main difference among the three modalities G60, G64 and G66 : Notes: In the above table, inside brackets, are reported the default values. The modality G60 is particularly indicate for general purpose mechanical high precision workings. The use of G64 is instead suggested in presence of canned cycles. In this case in fact the eventual position overshoot will be shadowed by the descent of the tool that will start immediately . In case of milling profiles generated by a CAM is normally preferable to use again the G64 because it also optimize the overall working time. However, if a higher precision is required, G66 can be used. As default the CNC forces the G64 modality.

G67 - Smoothing & Filtering interpolation Activation

<G67: ...> - Smoothing & Filtering interpolation Parameter Definition

G68 - Special interpolation Disabling

The G67 function sends in execution a “processor on line” that work at the Interpreter level. It inserts between every pair of linear elements of the profile (independently as they are oriented in the space), a rounding radius such to doesn’t exceed, with the associated chordal error a predefined error threshold. If enable the function acts also as filter removing from the input profile of the elements that have a length lower that a defined value. To enable the function it is enough to issue, alone on a line, G67. Before to do this should be necessary to change some of its configuration parameter. This operation can be done using the instruction <G67:…>. Finally to disable the Interpolation is necessary to issue, always alone on a line, G68. G67 configuration Syntax: <G67: Ec; Dist; Amin; Amax ; Npoint; Ax1; Ax2; Ax3 ; ON/OFF> Parameters description: Ec - Max accepted error on the profile, expressed in mm. Dist - Minimum distance, expressed in mm, under which the element will be discarded. Dist=0 means control disabled. Amin, Amax - Angles, expressed in degrees, inside which the Smoothing will be operative. Must be Amin (0.1°, Amax ( 179° . As default is proposed Amin=0.1° and Amax 60°. Npoint - Minimum number of points (sampling) requested to describe a rounding radius of Amax degrees. In the definition of Npoint it is better never go down 3°. To be more clear, if for example we have defined Amax=60° is better don’t define more that 20 as Npoint that just means 3° (60/20). Setting Npoint=0 the control is disabled. Ax1, Ax2, Ax3 - Labels of the axes where the G67 function will be applied. ON/OFF – Enables / disables the “Spline on Line” filter (see, for details description associated to <SPL:…> Instruction). It is an optional parameter. Example of Programming: <G67: 0.02; 0; 0.1; 179; 10; X; Y; Z; ON> ‘ Full format definition G67 ‘ Function activation G68 ‘ Function Disabling Note: In most practical cases working on Part Program generated through a CAD/CAM instead of G67 is suggested to use the newest G69 function.

G69 - PH interpolation Activation

<G69: ...> - PH interpolation Parameter Definition

The G69 function analyzes the programmed profile, that can include linear (G1) or circular (G2/G3) movements, generating as output a sequence of arcs (PH curves) that approximate the original path respecting a predefined chordal error. The “arcs” so obtained will be dynamically interpolated respecting the axes accelerations an max velocity. This will remove the discontinuity typical of a segmented profile making the resulting movement smooth and so allowing a higher working feed. So the use of G69 function is strongly suggested on milling process generated by CAM. This function will approximate the programmed points with a sequence of parametric curves. To enable the function it is enough to issue, alone on a line, G69. Before to this should be necessary to change some of its configuration parameter. This operation can be done using the instruction <G69:…>. Finally to disable the Interpolation is necessary to issue, always alone on a line, the G68 used also to disable the G67 Smoothing & Filtering interpolation. G69 configuration Syntax: <G69: AX=XYZ; E=err; P=nPoint; ANG=angMax; KAC=k;FIL=tFil; S=ON/OFF; G67=G67/G69; ANG1=angMin; ANG2=angMax; E2=err2> Notes: All the above parameters are optional and doesn’t require is respected a particular programming sequence. As separator character can be indifferently used the “semicolon” (;) or the “comma” (,). All numerical parameters can be set in parametric way. They accept in fact in input a “double” floating point variable. The G69 parameters, defined through the instruction <G69:…> can be programmed both one time at the CNC power–on (into the COSTUSER file), or generally, when necessary, inside the Part Program. In this last case the new programmed values will overwrite the foregoing one. Before to enable the G69 function, it is necessary to program, at least one time, the name of the associated axes setting the AX=.. parameter (example: <G69: AX=XYZ>). All the other G69 parameters, if not programmed, will assume the relative default values that are normally acceptable for the working. Parameters description: AX - Names of the axes involved in the parametric curves. Are foreseen the following situations: 2 linear axes in case of 2D workings. 3 linear axes in case of 3D workings. Note: the axes have to be programmed at least one time. E - Max accepted error on the profile [mm] (default: 0.01mm) Note: To optimize the G69 working is suggested to set this parameter with a value twice bigger than the tolerance (chordal error) set on the CAM to generate the Part Program. P - Number of points analyzed by the SW to “build” the parametric curves (default 300 points) with P=0 is assigned the default value. Note: To assign a value too big to this parameter can generate stop on the interpolated movements (due to the fact that the PH process, adding too much elements to the generating curve, isn’t able to supply enough curve functions to the interpolator. ANG - max angle over which the movement will be stop on the corner (default 90 degrees). ANG=0 assigns the default value. KAC - Multiplicative coefficient applied to the G69 axes nominal accelerations used on the definition of the profile feed and acceleration . Default value is 1. With KAC=0 is assigned the default value. Accepted range from 0 to 8. FIL - Type of Filter (default FIL=0) FIL=0 No filter enabled. FIL=1 “Noise” Filter enabled. It is suggested to use it with Part-Program typically generated by auto learn through a probe or a laser scanner. FIL=2 “Roughing” Filter enabled. It is suggested to use it during roughing steps when the profile must be the smoothest possible also maintaining the limitations imposed with the ANG1, ANG2 and E2 parameters (see description after). S - Spline on line filter enabling / disabling S=0N Spline filter enabled S=OFF Spline filter disabled Note: The “smoothing” degree associated to the Spline on line filter is set through the instruction <SPL:Pn> (See after for a specific description), where “n” can assume a value inside the range from 1 to 20. Bigger is the value, higher will be the smoothing effect of the filter and the associated noise reduction, but also less precise the obtained profile. As default with the G69 the Spline on line filter is enabled with a degree of 3 (S=ON and <SPL:P3>) G67 - Management of G67 Function G67=G67 G67, if programmed, will work as usual (default value). G67=G69 G67, if programmed, is managed as G69. So programming G67 we will obtain the same effects than programming the G69. The following parameters have a meaning only programming the “Roughing filter” ( FIL=2 ANG1 - Minimum angle overcoming which is applied the “Roughing” modality. In other words is applied a rounding Radius on the corner however warranting the tolerance defined with the E2 parameter. (Default: 20 degrees). Note: Setting low values on ANG1 parameter we obtain: - Smoother working profiles. - Bigger form error. - Generally a more continuous motion. ANG2 - Max angle overcoming which isn’t applied the “Roughing” modality. (Default: 120 degrees) E2 - Max. error on the corners [mm] in case of angles bigger than ANG1 and smaller than ANG2. (Default: 1 mm). Note: The E2, ANG1 and ANG2 values are functions of the type of working . Typical values if a good precision is required are: E2=0.050, ANG1=20 and ANG2=60 .

<SPL: ...> - Spline on line management

This function allows to reduce the spike on the acceleration at level of single axis, during interpolation. To maintain in fact a feed and acceleration sinusoidal characteristic, when executing a generic profile, doesn’t mean that also at single axis level happens the same. The <SPL:…> function so works as a programmable filter through a parameter called “Smoothing Factor”. Syntax: <SPL:ON; PN; Ax0[;Ax1;…;Axn]> Parameters description: ON/OFF – Optional parameter used to enable / disable the function. Pn - Optional parameter used to define the Spline Smoothing Factor It specify, using as measurement unit the CNC tick (Tcyc), how often will be acquired the Spline control points . So the interpolation points will be computed every tick but using the control points acquired every Pn *Tcyc The parameter Pn can assume values in the range from P1 to P20. Without to program this parameter, as default the CNC will be assumed Pn=KT, that mean that the control points are acquired any Tau ( KT * Tcyc). Increasing it the acceleration spikes are reduced but the obtained profile will be less precise. However the most important effect of the filtering will be a reduction of the mechanical noise during movement and consequently the possibility to set higher accelerations. AXn - List of axes (are indicated the relative labels) where the function will be applied. Some programming examples: <SPL:ON; P4;X;Y;Z > ‘ Generic form <SPL: X;Y;Z> ‘ Only axes selection <SPL:ON> ‘ Only activation <SPL:P5> ‘ Only definition of the “Smoothing Factor”

# Instructions for Origin management

G59 X.. Y.. Z.. - Apply an offset to the active Origin

Through this instruction it is possibly to apply, to the active origin, an absolute or incremental, offset . Are accepted the following syntax: G59 X.. Y.. Z.. or G59 DX.. Y.. Z.. or G59 X.. DY.. Z.. or other possible combinations of absolute/ incremental programming . Where DX.., DY.. and DZ.. represent incremental offset, respectively to X, Y and Z current position. Example: N.. G59 X30Y80 The new reference system is obtained from the active one through a translation on X30 and Y80.

G59 Nxx X.. Y.. Z.. - Loading of origin Nxx

Through this instruction it is possible to load the origin’s values . In this way one or more Origins can be for example, loaded directly by a CAM SW. Example: G59 N3 X0 Y0 Z0 Load the Origin 3 forcing 0 to X, Y and Z current quotes.

G58 X.. Y.. RC.. - Apply an offset + a rotation to the active Origin

Through this instruction it is possibly to offset and contemporary rotate, on the Contouring Plane, the active origin. The offset + rotation can be both expressed in absolute or incremental format. Assuming XY the active Contouring Plane are in fact accepted the following syntax: G58 X.. Y.. RC.. or G58 DX.. DY.. RB.. and all their composite expressions. We remember that RC.. represents an absolute angle of rotation, while DX.., DY.. and RB.. are respectively incremental offset in X and Y and an incremental rotation expressed in degrees. Example: N.. G58 X30 Y80 RC30 The new reference system is obtained from the active one Moving it at X80 and Y30 and after applying an anti clockwise rotation of 30°. For a correct utilization of G58 function: It isn’t allowed to add other instructions in the same block that contains a G58.. When a G58 is active isn’t allowed to change the contouring plane, with G16.., G17.., G18.. or G19, or to modify /change the active origin through the instructions G54 or G59. When a G58 is active isn’t allowed to activate/deactivate a Static or a Dynamic Transformation Arrays. The G58 can be however used to define a profile that will be mirrored or scaled through the MIR or SCALE functions. The G58 works before GAP Profile Programming Instructions. So if G58 is issued during a profile programming (described through GAP), only the after going blocks will be affected by the rot-translation introduced with the G58. The Virtual elements defined through EXPERT instructions take care of the rot-translation eventually active during their definition. They doesn’t be modified when G58 is deactivated or modified.

G58 - Reset all rot - translations

Through the instruction G58 (written alone) it is possible to reset all rot- translations eventually active (programmed through the G58 …. full format instruction).

G53 - Forces Absolute Machine Origins

The instruction G53 forces as reference the Machine Zero set by the manufacturer of the Machine Tool. This instruction, normally not used in a Part Program, causes a momentary suspension of the active origins (selected by using G54.XX) and eventually translated or rot-translated (using G59 and G58). The G53 however does not cancel any enabled Radius and Tool Length compensations, as well as active Mirror feature and Static/Dynamic Matrixes which effect the positioning of the tool. For example, programming: N...G53 X2000 Y1850 The M.T. positions itself at the quotes X2000 and Y1850 in respect to the physical Machine Zero.

# Instructions for Tools Radius and Length compensation  management

D0 - Tool length compensation suspension

When a tool is loaded through the instruction Tx M6, automatically the CNC, using the Length L read from the Tool Table related to the loaded tool, makes active the length compensation on the vertical direction (typically along Z). The length compensation can be momentary suspended through the D0 command.

G43 - Set Tool Length compensation along positive direction

G43 applies the tool length compensation along the positive direction of the axis which immediately follows the instruction. Example: N30 G01 G43 Z-50 X100 ‘Inserts the length compensation in a positive direction along the Z axis.

G44 - Set Tool Length compensation along negative direction

G44 applies the tool length compensation along the negative direction of the axis which immediately follows the instruction..

<DRA: nn> - Profile stock definition

Through the parameter nn is defined the entity, in mm, of the stock that must be left on executing the programmed profile . <DRA:0> is the default value set by the % command. The parameter nn can assume also negative values. In this last case the profile will be reduced of the nn entity. The instruction is often used to allows tool radius compensation without to have physically installed a tool on the spindle.

<DLN: nn> - Profile stock in dept

Where “nn” " represents the integer machining allowance which will be left along the depth axis. In other words the along the axis Compensated in Length defined through the instructions G43 or G44 or G16.... <DLN:0> is the default value set by the % command.

# Instructions to load  Tools Parameters from a File

G795 - Starts a Loading tool procedure

The complete syntax of the command is the following: G795 Sequence of G79x specific commands (see for details next paragraphs)

G797 - Loads Parameters of a new Tool

The complete syntax of the command is the following: <TPC=..> <TTC=..> <POS=..> <FOR=..> <SIZ=..> <MCT=..> <TRN=0> G797 Where: TPC = Tool Physical Code TTC = Tool Logical Code (T) POS = Position of the tool in the Warehouse (in case of Tool out of the Warehouse POS=7000) FOR = Tool Shape, more specifically: FOR=1 ( Spherical tool FOR=2 ( Cylindrical tool FOR=3 ( Thoroidal tool FOR=4 ( Bit FOR=5 ( Male FOR=6 ( Probe SIZ = Tool Dimension, more specifically: SIZ=0 ( Tool “Small” SIZ=1 ( Tool “Medium” SIZ=2 ( Tool “Big” SIZ=3 ( Tool “Extra” Note: In case of tool out of the warehouse the SIZ field must be ofsetted of 10 MCT = 0 ( Normal tool MCT = 1 ( Multi-cut tool TRN = 1 ( Fix value Examples: <TPC=2> <TTC=2> <POS=2> <FOR=2> <SIZ=0> <MCT=0> <TRN=0> G797 It allows to insert the tool T2 (a cylindrical tool) specifying that its place is 2, that is a small tool and no multi-cut.

G798 - Loads / Modifies Geometrical Parameters of a Tool

The complete syntax of the command is the following: <TPC=..> <TTC=..> <LUN=..> <RTA=..> <RAD=..> G798 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) LUN = Tool Length (in mm) RTA = Cutting radius. Valid only in case of milling Tool . For cylindrical tool RTA = 0. For spherical tool RTA=RAD. RAD = Tool Radius (in mm). Example: <TPC=3> <TTC=3> <LUN=100.000> <RAD=5.000> G798 It defines the tool T3 with Length = 100 mm, and Radius 5 mm.

G792 - Associates a comment to a Tool

The complete syntax of the command is the following: <TPC=..> <TTC=..> (Comment) G792 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) Comment= the associated comment string (max 30 chrs) Example: <TPC=3> <TTC=3> (Spherical Tool with Radius 5 mm) G792

G799 - Loads Wear & Life parameters

The complete syntax of the command is the following: <TPC=..> <TTC=..> <ATL=..> <WTL=..> <MXL=..> <MXR=..> <MXP=..> <MXU=..> G799 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) ATL = Tool Expected Life (in sec) WTL = Life Warning Threshold (in sec) - Optional parameter MXL = Max Length Wear (in mm) MXR = Max Radius Wear (in mm) MXP = Max Wear first time (in mm) – Optional parameter MXU = Max one time Wear (in mm) – Optional parameter Example: <TPC=16> <TTC=16> <ATL=10000> <WTL=9900> <MXL=0.012> <MXR=0.011> <MXP=0.016> <MXU=0.014> G799 Note: The command can be used only if the “Wear & Life Management Option” is enabled.

G791 - Loads Tool Configurable Parameters

The complete syntax of the command is the following: <TPC=..> <TTC=..> <PGA=..> <PGB=..> <%%PGC=..> <%%PGD=..> G791 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) PGA = Configurable Custom Floating type Parameter1 PGB = Configurable Floating type Parameter2 %%PGC = Configurable Long type Parameter3 %%PGD = Configurable Long type Parameter4 Example: <TPC=12> <TTC=12> <PGA=100.042> <PGB=99.004> <%%PGC=12300> <%%PGD=23450> G791

G794 - Loads / Removes a tool to/from the warehouse

The complete syntax of the command is the following: <TPC=..> <TTC=..> <POS=..> G794 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) POS = Tool Warehouse place ( 7000 if the tool is out of the warehouse) Examples: <TPC=10> <TTC=10> <POS=5> G794 ‘ We want to load the tool T10, defined as outside warehouse, into position 5 <TPC=20> <TTC=20> <POS=7000> G794 ‘ We want to remove the tool T20 from the warehouse

G793 - Deletes a Tool

The complete syntax of the command is the following: <TPC=..> <TTC=..> <POS=..> G793 Where TPC = Tool Physical Code TTC = Tool Logical Code (T) . If we specify only this parameter and it refers to a multi-cut tool, the tool is however removed. POS = Tool Warehouse place Examples: We want to delete the following Tools: Family T1 composed by 3 Tools (TPC= 1, 11, 111) Corrector D10 Tool T20 located in place 5 of the Warehouse Multi-cut TPC=5 (T= 5,15,25) To do this we will write the following procedure: G795 ‘ Start procedure <TTC=1> G793 ‘ Remove family T1 <TTC=10> G793 ‘ Delete Corrector D10 <POS=5> G793 ‘ Delete tool T20 <TTC=5> G793 ‘ Remove the multi-cut tool TPC=5 Note: The Tool currently active (mounted on the spindle) cannot be cancelled.

# Interpolation  and Contouring Plane  definition

G16 Axis1 Axis2 Axis3 +/- - Free selection of Contouring Plane

Axis1 and Axis2 identify the Contouring plane Axis3 is the axis where is applied the Tool Length Compensation, +/- the direction where it is applied Example: G16XZZ+ It means : Contouring Plane XZ, tool length compensation applied along Z axis in positive direction.

G17 / G18 / G19 - Standard Contouring Plane definition

The definition of the Contouring Plane forces also the sense of rotation clockwise (G03) of the circular interpolation, as graphically showed by the picture: In case of XYZ milling machine G17 is the default programming. G17 Contouring Plane XY – Abscissa X, Ordinate Y G18 Contouring Plane ZX – Abscissa Z, Ordinate X G19 Contouring Plane YZ – Abscissa Y, Ordinate Z

G00 / G0 X.. Y.. Z.. - Rapid Traverse Interpolation

Other accepted programming Syntax: G0 DX.. DY.. Z .. or G0 X.. Y.. DZ.. or G0 X.. DY.. Z.. or all other possible combinations. DX.. DY.. and DZ.. are incremental movements on X, Y and Z.

G01 / G1 X.. Y.. Z.. - Linear interpolation at programmed Working Feed (F…)

Other accepted programming Syntax: G1 DX.. DY.. Z.. or G1 X.. Y.. DZ.. or G1 X.. DY.. DZ.. or all the other possible combinations. DX.. DY.. and DZ.. are incremental movement on X, Y and Z. Are also supported the following other definitions of a linear interpolation: G1 X.. RC.. G1 Y.. RC.. G1 X.. Y.. RC.. G1 RC.. D..

G02 / G2 I.. J.. XP2 YP2 - Circular clockwise interpolation at Working Feed into XY Contouring Plane

Where: I.. Centre Coordinate in X direction of the Arc J.. Centre coordinate in Y direction of the Arc XP2 Coordinate of the Arc final Point P2 YP2 Coordinate of the Arc final Point P2 Notes: The coordinate I.. and J.. can be expressed in different ways: Always absolute (default) Always incremental (through a specific setting) Conditioned by the programming (by G90 and G91 auxiliary functions) The coordinates of the end point can also be expressed incrementally in relation to the starting point (P1) by using the parameter D... For example, the following definition are accepted by the CNC: G02 I... J... XP2 DY... G02 I... J... DX... YP2 G02 I... J... DX... DY... The ECS CNC supports also the following other definitions of an arc interpolation ( in case of XY Contouring Plane): G02 X.. Y.. R.. [K] G02 I.. J.. RB.. G02 I.. J.. RC.. G02 R.. RB.. G02 R.. RC..

G03 / G3 I.. J.. XP2 YP2 - Circular anti-clockwise interpolation at Working Feed into XY Contouring Plane

For more details see description associated to G02/G2 Clockwise interpolation

G10 Xpole Ypole a.. b.. - Rapid Traverse movements using Polar Coordinates

Where: Xpole ... Ypole.... Absolute co-ordinate of the pole referred to the active origin a .... Polar angle (in degrees) e .... Polar radius

G11 Xpole Ypole a.. b.. - Linear movement at working Feed using Polar Coordinates

The parameters have the same meaning already described in case of Rapid Traverse movement instruction (G10)

G12/ G13 I..J.. Xpole Ypole a.. b.. - Clockwise / Anti-clockwise circular interpolation using Polar Coordinates

Where: I.. J.. (or K..) Absolute co-ordinate of the centre of the circle referred to the active origin Xpole ... Ypole.... Absolute co-ordinate of the pole referred to the active origin a .... Polar angle (in degrees) e .... Polar radius

RA.. - Insertion of a Rounding Radius between two geometrical elements

Syntax: <First Geometrical Element definition > RA [+/-] ... <Second Geometrical Element definition> Through the sign it is possible to define the sense of rotation of the Rounding Radius. It will be positive in case of anti clockwise sense of rotation, negative vice versa, in case of clockwise rotation. A positive sign can be omitted. In case of Rounding Radius between two lines the sign can be also omitted (it will be in fact automatically detected by the CNC). A Rounding Radius can be inserted between two contiguous geometrical elements. It can be applied between: 1) Two linear elements 2) A line and an arc 3) Two arcs

SM.. - Insertion of a Chamfer between two linear elements

Syntax: <First Linear Element > SM ... <Second Linear Element> Programming Example:

# Tool Radius Compensation and Profile Attach / Detach

G41 - Tool Compensation ON - Working Piece at right side of the tool

G42 - Tool Compensation ON - Working Piece at left side of the tool

These commands activate the Tool Radius compensation attaching the programmed profile through a straight G01movement. Note: When evaluating the reciprocal Tool / Piece position, it must be considered that the tool will be observed from the tool and in the direction of the machining execution. To properly use the G41 and G42 instructions must be respected the following rules: 1. Define the Contouring Plane through the instructions (G16 .. or G17or G18 or G19). 2. Position the axes of the Contouring Plane (in G00 orG01) at a distance, from the profile, which is at least equal to the Tool radius. 3. Position the axes on the starting point (in G00 or G01). On the same block it is suggested to activate the tool radius compensation through the instructions G41 or G42. They can however be inserted alone in a separate line. The axes will reach the programmed contouring starting point with the tool tangential to the profile and feed 0. The attach to the profile can take place either on a straight line or on an arc and at any point. After G41 or G42, it is necessary to insert a working movement (G01, G02 or G03) on the Contouring Plane. At the end of the contouring, the tool will be detached from the profile using the instructions G00 or G01, at the same time the Radius Compensation must be cancelled through the instruction G40 (see for details next paragraph). In this case, at the end of the detach movement, the centre of the tool will be on the programmed co-ordinates. Example: Notes: When, to program the profile, are used GAP or EXPERT geometrical languages, it is possible, instead to directly define the profile starting point, choose one of the following alternatives: To program the tool to attach the profile with a trajectory orthogonal to a defined element. In this case the programming syntax becomes: To program the tool to attach the profile staying tangent at two defined contiguous elements . In This case the programming syntax becomes: where both Element1/ 2 can be Lines or Arcs defined in all possible syntax foreseen by ISO, GAP and EXPERT languages. Note: Through a specific setting ( key AGAP =N into the GEN.TAR configuration file) it is also possible to instruct the CNC to understand the programmed point before the G41 / G42 as the starting point of the first element where radius compensation must be applied. In this way the point programmed immediately after G41/G42 will be reached with compensation already active

G40 - Tool Radius Compensation OFF

The G40 code will be inserted, after the programming of the last point of the profile, into a new line containing the co-ordinate of the point to be reached with compensation OFF. Typically in the same line is inserted also G00 to execute the movement in rapid. When, to program the profile, are used GAP or EXPERT geometrical languages, it is possible, instead to directly define the profile leaving point, choose one of the following alternatives: To program the tool to detach the profile with a trajectory orthogonal to the last element defined. In this case the programming syntax becomes: To program the tool to leave the profile staying tangent at two programmed contiguous elements . In This case the syntax becomes: Element n G40 Element n+1 X… Z… or Element n G40 Element n+1 X… Z… Note: In case of setting of the key AGAP =N into the GEN.TAR CNC configuration file, the last point of the profile, placed before G40 , will be reached with radius compensation active but, from this point it will be deactivated.

G47 - Tang. Attach with Tool Comp. ON - Work. Piece at right side of the tool

G48 - Tang. Attach with Tool Comp. ON - Working Piece at left side of the tool

These commands activate Tool radius compensation attaching the programmed profile through a tangential movement (G02/G03). Example: Note: When, to program the profile, are used GAP or EXPERT geometrical languages, it is possible, instead to directly define the profile attach point, to directly program the element of the profile that we desire to attach. In this case the programming syntax becomes: G47 (or G48) K Element 1 The attach modalities will respect the rules of the standard G47 / G48 attach with the only difference that as starting point on the profile is chosen the one obtained as intersection between the Element 1 and the orthogonal to it passing on the point where the center of the tool has been moved before issue the G47 / G48 instructions. In case the Element1 is a circle, normally applying the above rules we have 2 solutions, so as starting pint will be chosen the nearest .

G46 - Tangential Detach reaching the programmed point with Tool Comp. OFF

The G46 code will be inserted , after the programming of the last point of the profile, into a new line containing the co-ordinate of the point to be reached with detaching tangentially the profile with compensation OFF. Typically in the same line is inserted also G00 to execute the straight part of the movement in rapid. Notes: When, to program the profile, are used GAP or EXPERT geometrical languages, it is possible, instead to directly define the profile detach point, to directly program the element of the profile from which we desire to detach. In this case the programming syntax becomes: Automatically is defined on Elementn a point that linked to X.. Y.. identify an orthogonal line to Elementn. Such point will be used to detach the profile.

<TGR: K; Angle> - Programming of Radius and Angle of attach

Through this instruction it is possible to define the characteristic of the Tangential Attach / Detach programmed with G46, G47 and G48. Specifically it is possible to set the Radius as K times the Tool radius and directly to define the Angle described by the attach arc. As default K is set = 2 (in the radius computation is also taken in account the overstock eventually programmed with the <DRA:…> instruction). Default angle value is instead 90°. Note: The instruction <TGR:K;angle> must be programmed on the same block that contains the G46, G47 and G48. Example:

# Canned Cycles

Generalities on Canned Cycles

After definition a Canned Cycle remains active till it is executed one of the following instructions : G80, %, M02, M30 or another Canned Cycle. Till a Canned Cycle is active all movements of the axes of the contouring plane, will generate, at the and of the movement, its execution. For this reason it is strongly recommended, to avoid undesired executions, to disable them before all Tool change commands. The variables used by Canned Cycles are “Retentive” type, so at the power-on they still contains the valued loaded before the foregoing power off. It is important to take care also of this characteristic to avoid undesired behaviours. Before program a canned cycle it is necessary to define the contouring Plane and the axis and the direction where will be applied the tool length compensation .

<CFF=CF Axis> - Definition of the Axis along which Canned Cycle will be applied

Examples: <CFF = CFZ> The Canned Cycles are assigned along Z axis. <CFF =CFY> The Canned Cycles are assigned along Y axis.

G81 - Standard Drilling

The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G81 <ENT=..> <RAP=..> <RAL=..>

G81/3 - 3 Layers Drilling

With this cycle it is possible to drill holes defining two zones where the bit will advance at different feeds ( normally lower) than the one programmed with the F… instruction. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G81 <ENT=..> <RAP=..> <RAL=..> <SF1=..> <FE1=..> <SF2=..> <FE2=..>

G82 - Drilling with Dwell for chip breaking

The only difference between this cycle and the standard drilling G81 is the dwell done by the bit after it reached the Depth quote (ENT) to broken the chip. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G82 <ENT=..> <RAP=..> <RAL=..> <TIM=..>

G83 - Deep Drilling with clearing

This cycle is normally used to drill deep holes. The first drill the bit will reach the quote defined with the parameter INI. After it will go back in rapid to the RAP quote. Next time the bit will advance of the entity given by (INI + IND) . After again it will go back to RAP. The operation will be repeated reducing every time the increment IND till the ENT quote will be reached. Note: When the increment reaches a value smaller than IND it will be forced equal to IND . The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G83 <ENT=..> <RAP=..> <RAL=..> <INI=..> <IND=..>

G83/r - Deep Drilling with Dwell for chip breaking

The differences between this cycle and the deep drilling G83 are: At the end of every drilling step it is executed a dwell of TIM sec to broken the chip. At the end of the dwell the bit isn’t moved in rapid to the RAP quote but starts immediately next drilling step. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G83 <ENT=..> <RAP=..> <RAL=..> <INI=..> <IND=..> <TIM=..>

G84 - Tapping

This cycle is used to tap when the Milling Machine spindle is not equipped with of a position transducer. In this case it is suggested also to use a tap with a mechanical compensator . It is also necessary to verify that: Programmed Feed [mm/min] = Programmed Speed [rpm] * Tap Pitch [mm] Note: The return movement between ENT and RAP is done at working feed reversing the spindle sense of rotation. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G84 <ENT=..> <RAP=..> <RAL=..>

G85 - Boring

The only difference between this cycle and the Standard Drilling G81 is that the tool return to RAL quote is done at working feed, between ENT and RAP, and at rapid (G00) from RAP to RAL. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G85 <ENT=..> <RAP=..> <RAL=..>

G86 - Boring with Spindle stop

The only difference between this cycle and the Standard Drilling G81 is that the spindle, reached the ENT quote is stopped It will restart only when the tool reaches in rapid the RAL quote. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G86 <ENT=..> <RAP=..> <RAL=..>

G87 - Boring with Retraction

This cycle differs from the “Boring with Spindle Stop” G86 because in this case, when tool reaches the ENT quote, the spindle is not only stopped, but oriented in a specific position (through the M19 Function), disengaged with a movement in X and Y and finally moved in Rapid to the RAL quote. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G87 <ENT=..> <RAP=..> <RAL=..> <DAX=..> <DAY=..>

G89 - Boring with Dwell

This cycle differs from the standard Boring cycle G85 allowing to program a dwell time (TIM sec) between the arrival to the ENT quote, to the start of the movement, done at working feed, to reach the RAP quote. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G89 <ENT=..> <RAP=..> <RAL=..> <TIM=..>

G80 - Cancel Canned Cycles G8x

G184 - Solid Threading

This cycle requires a spindle equipped with a position transducer. The CNC has in fact to synchronize the position of the spindle with the one of the vertical axis (typically Z). The cycle G184 requires that the spindle is set in G94 mode (rpm). To cancel a G184 cycle is necessary to issue a G150 instruction. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G184 <ENT=..> <RAP=..> <RAL=..> <SPD=..> <PCH=..> <ROT=..> <DAX=..>

G184/r - Solid Tapping

This cycle requires a spindle equipped with a position transducer. The CNC has in fact to synchronize the position of the spindle with the one of the vertical axis (typically Z). The cycle G184/r requires that the spindle is set in G94 mode (rpm). To cancel a G184/r cycle is necessary to issue a G150 instruction. The cycle Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: G184 <ENT=..> <RAP=..> <RAL=..> <SPD=..> <PCH=..> <ROT=..>

# Pocket Milling Macros

## G88 - Boring of an internal Hole

The Macro G88 allows to bore  a hole with cylindrical / toroidal tool simply positioning it on the axis hole.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G88 <ENT=..> <RAP=..> <RAL=..> <DIA=..> <ROT=..>

## G188 - Cylinder External Milling

The Macro G188 allows to finish  an external cylinders, defining the attach angle.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G188 <ENT=..><RAP=..><RAL=..><DIA=..><ROT=..><SME=..><ANA=..><KFD=..><DRA=..><INI=..><ASF=..><ALT=..>

SME – Stock allowance present on the work piece                         ANA – Attach angle

KFD – Feed modifier coefficient applied on attach phase               DRA – Stock allowance to be left after working

INI  - Defines the applied constant increment in depth. It takes place from RAP to ENT quotes. INI=0  means  single pass.

ASF – Defines the eventual  inclination of the surface. For a cylinder is ASF=0.

ALT – Height  of the Cylinder . It is  not  necessary to  program if ASF=0.

## G185 - Roughing of a Rectangular Pocket with central pre-drilling

The Macro G185 allows to roughing a rectangular pocket independently as it is orientated on the Contouring Plane. It requires  an adequate pre-drill  in the centre of the pocket.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G185 <ENT=..><RAP=..><RAL=..><ROT=..><ANA=..><DAX=..><DAY=..><RAG=..><DRA=..><INI=..><ASF=..><ALT=..>

DAX – Side of the pocket in mm along the abscissa (X)  before apply the ANA rotation.

DAY – Side of the pocket in mm along the ordinate (Y) before apply the ANA rotation.

RAG – Rounding radius applied on the pocket corners.

INI  - Defines the applied constant increment in depth. It takes place from RAP to ENT quotes. INI=0  means  single pass.

ASF – Defines the eventual  inclination of the pocket border  surface. Values accepted  between 0° and 80°.

ALT – Height  of the Pocket . It is  not  necessary to  program this parameter  if ASF=0.

DRA – Stock allowance to be left on profile.

## G186 - Finishing of a Rectangular Pocket

The macro G186, allows the finishing  a Rectangular pocket using   both Toric or Spherical tools and guaranteeing a  programmed  max peak height, between two contiguous  passes.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G186 X.. Y..

<ENT=..><RAP=..><RAL=..><DIA=..><ROT=..><SME=..><ANA=..><KFD=..><DRA=..><RGS=..><ASF=..><ALT=..><RUT=..>

X..Y.. – Coordinate of the pocket centre from which will start the attach movement.

SME – Stock allowance present on the pocket .

## G187 - Roughing of a Circular “Bean Shaped” Pocket

<The Macro G187 allows to roughing a Circular  “Bean Shaped”  pocket . The macro requires  an adequate pre-drill  in the attach point P.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G187 X.. Y..  I.. J..

<ENT=..><RAP=..><RAL=..><DIA=..><ROT=..><ANA=..><KFD=..><DRA=..><INI=..><ASF=..><ALT=..><RIC=..>

DIA – Width of the pocket [mm]

I.. J.. -  Absolute coordinate of the  centre of the concentric arc that define the pocket (C).

X..Y.. – Coordinate of the attach point (P)

KFD – Feed modifier coefficient applied during the depth descent phase.

INI  - Defines the applied constant increment in depth. It takes place from RAP to ENT quotes. INI=0  means  single pass

ASF – Defines the eventual  inclination of the pocket  border  surface. In case of straight  borders   is ASF=0.

ALT – Height  of the Pocket. It is  not  necessary to  program if ASF=0.

DRA – Stock allowance to be left on profile [mm].

RIC – Minimum Overlap [mm] between  consecutive passes.

## G189 - Roughing of a Circular Pocket with central pre-drilling

The Macro G189 allows to roughing  a circular pocket, positioning the tool on its centre. This  requires that a  pre-drill must be done.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G189 X.. Y..

<ENT=..><RAP=..><RAL=..><DIA=..><ROT=..><SME=..><KFD=..><DRA=..><INI=..><ASF=..><ALT=..><RIC=..>

KFD – Feed modifier coefficient applied on attach phase               DRA – Stock allowance to be left on profile.

INI  - Defines the applied constant increment in depth. It takes place from RAP to ENT quotes. INI=0  means  single pass.

ASF – Defines the eventual  inclination of the surface. Values accepted  between 0° and 80°.

ALT – Height  of the Cylinder . It is  not  necessary to  program if ASF=0.

RIC – Minimum Overlap [mm] between  consecutive passes.

## G190Finishing of a Circular Pocket

The Macro G190 allows the finishing of a circular pocket with the use of  Toric or Spherical tools. In case  of finishing of a conic surface  can be  programmed a max the  peak height between  two contiguous   passes.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G190 X.. Y.. <ENT=..><RAP=..><RAL=..>

<DIA=..><ROT=..><SME=..><KFD=..><DRA=..><RGS=..><ASF=..><ALT=..><RIC=..><RUT=..><SME=..>

## G175 - Roughing of a Rectangular Pocket with concentric passes

The Macro G175  allows to roughing  a rectangular  pocket, executing  concentric passes with a progressive increment in depth, following, on this movement, a programmed inclination  angle.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G175  X.. Y..

<ENT=..><RAP=..><RAL=..><ROT=..><ANA=..><DAX=..><DAY=..><RAG=..><DRA=..><INI=..><ASF=..><ALT=..><ANL=..>

Note:  Using the Macro G175 the tool  radius compensation  (G41, G42, G46 and G47) hasn’t to be active

## G179 - Roughing of a Circular Pocket with concentric passes

The Macro G179 allows to roughing  a circular pocket, executing  concentric passes with a progressive increment in depth, following, on this movement, a programmed inclination angle.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G179 X.. Y..

<ENT=..><RAP=..><RAL=..><DIA=..><ROT=..><SME=..><KFD=..><DRA=..><INI=..><ASF=..><ALT=..><RIC=..> <ANL=..>

Note:  Using the Macro G179, the tool  radius compensation  (G41, G42, G46 and G47) hasn’t to be active.

## G150 - Cancels Macro / Canned Cycles  from G151 to G199

## L<MILL> - Internal/External Flattening of a Rectangular Area

The macro “MILL” allows to   flattening  a rectangular area, executing “fret pattern” passes with a progressive increment in depth.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

Syntax:

G189 <INX=..><INY=..><DAX=..><DAY=..><ENT=..><RAP=..><RAL=..><INT=..><RIC=..><KFD=..>

INX /INY   window starting corner expressed as   contouring plane axes  co-ordinates.

DAX/DAY windows end corner expressed as contouring plane  axes  co-ordinates .

INT flag that  to define attach  conditions. INT=0  ( internal tangential attach  INT=1 ( external attach with a safety distance of 2 mm.

RIC desired overlap between two contiguous passes.

KFD – Feed modifier coefficient applied on the entry movement from RAP to ENT.

## G778 - Emptying  of a generic profile pocket – Without finishing step

## G779 - Emptying  of a generic profile pocket – With finishing step

## G777 - Definition of parameters used by macro G778 and G779

## G701 - Definition of pocket and islands profiles used by macro G778 and G779

The  G778  macro  allows to empty a pocket delimited by a generic profile. Inside the pocket can be defined (always through generic profiles)  till 26 “islands” where material haven’t to be removed.

Depth increment is freely programmable and  is always carried out on a definite point. Also working inclination can be programmed.  Each pass is carried out contouring by first  the external pocket  profile, then islands are contoured  and finally pocket  will be emptied  respecting the  programmed inclination angle.

The G778 macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

The G779  macro  is similar to the G778 but allows also to Finishing  the  pocket

The G779 macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

The G777 is instead an associated function that allow, both in case  of  G778 or G779 programming, to define the necessary  parameters.

Syntax:

G777 <QFO=...> <QIN=...> <PPA=...> <QPO=...> <APA:...><KPE:...> <DQS=...>  <DRA:...> <KFE=...>

KPE – Path Coefficient. It defines how the milling tool  has to manage  the start  of a next step.

If the length of the working  profile to reach  the next end point  is smaller  or equal  to KPE  times their distance in air, the milling tool  will follow directly the profile   Otherwise the tool  will be lifted, at rapid speed, to the QPO quote, it will move on the vertical starting point of the new step, it will descend in rapid to the safety distance DQS from which it will start to move to the programmed  working feed. KPE can also assume some particular values:

If  KPE=0 movements will be done always on the air to the  QPO quote.

If  KPE=100  movements will be always  following the profile without  lift the tool.

If KPE=-1, the times for carrying out the 2 above alternative are calculated and the shortest one is chosen (default).

DRA – Surplus stock. This parameter  must be programmed only if a Finishing step is foreseen . So only in case a  G779 is  programmed.

KFE - Feed modifier coefficient applied on the start cutting movements  (default  KFE=1).

DPA - Distance between two contiguous pass  expressed in "milling radius" . As default is  DPA=1.6 ( so the distance between two steps will be  1.6* milling radius).

Finally one or more G701  will allow to define the pocket and /or islands profiles  used both by the G778 or G779 macros.

Syntax:

G701  XAT.. YAT..

External or Island’s profile

Notes:

XAT..YAT  - Attach point to the pocket  or island profile.

After the G701 function, the pocket or the island profile must be programmed using  ISO or GAP/EXPERT geometrical languages. For a more clear  programming is also suggested to define the profile as sub-routine.

Both type of profile ( to define pocket and islands)  must be closed type. Important - They must result closed also in case  the tool radius compensation is applied.  There are no limits as to the number of elements making up the groove and island profile.

G778  Programming example:

‘Main Program

%

N5   G16XYZ*

N10 M6 T1 F500

N20 M3 S1500

N30 G0 X0 Y0 Z100

‘ Parameter definition

N40 G777 <QFO=20> <QIN=40> <PPA=8> <QPO=50> <APA=30> <KPE=10> <DQS=5> <DRA:0> <KFE=10><DPA=1.6>

‘ External Profile definition

N50 G701 <XAT=-230> <YAT=0>

N60 L<CIRCLE>

‘ Internal Island Profile definition

N70 G701 <XAT=220>  <YAT=0>

N80 L<ISLAND>

‘ Machining start

N80 G778

N90 M2

‘CIRCLE   Sub Program  - Profile defined  using EXPERT geometrical  language

N10   O5 = G2 I0 J0 R250

N20   P2 =  X-250 Y0

N30   G1 G48 P2

N40   O5

N50   P2

N60   G46 X-230 Y0

N70   <RET

“ISLAND” Sub Program – Profile defined using EXPERT geometrical language

N10   O1 = G3 I150 J0 R50

N20   O2 =  G3 I0 J150 R50

N30   O3 =   G3 I-150 J0 R50

N40   O3 =   G3 I0 J-150 R50

N50   L1  =   G1 X150 Y 50 RC180

N60   L2  =   G1  X–50 Y 150 RC90

N70   L3  =   G1  X-50  Y150 RC-90

N80   L4   =  G1 X-150 Y-50 RC0

N90   P1   =  X200 Y0

N100 G1 G49 P1

N110 O1

N120 L1 RA20

N130 L2

N140 O2

N150 L3 RA20

N160 L1

N170 O3

N180 L4 RA20

N190 L3

N200 O4

N210 L2 RA20

N220 L4

N230 O1

N240  P1

N250  G46 X220 Y0

N300 <RET>

## G722 - Machining of Truncated Conical Surface (Archimedean  Spiral)

The G722  macro  allows to machine a pocket  or a truncated-conical relief developing an Archimedean spiral profile.

The macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

The recognition of the type of surface to be produced (pocket  or relief) is automatic on the basis of  the start and end  spiral quotes.

Through the %FON  parameter the programmer can also to define if  he  intends to work the surface respecting the final programmed dimension (even if the final dimension is “pierced” by part of the tool) or if it is requested  that the dimension set for the bottom is not exceeded.

Syntax:

G722 I..  J..  <RIN=..><RFI=..><ROT=..><QIN=..><QFI=..><%FON=..><DPA=..>

ROT - Working Direction. ROT=3 (default) defines anti-clockwise sense of rotation while ROT=2 a clockwise one.

%FON - define as we desire to finish the Spiral bottom. %FON=0  if we want that the programmed bottom of the spiral (lower between QIN an QFI quotes) is physically guaranteed (also if this means some piercing on the Spiral bottom). %FON=1 (default) if we want instead never exceed the programmed Spiral bottom.

Programming Example:

%

N10 G16XYZ+

N20 M6 T1

N30 Z50

N40 G0 X0Y0

N50 F1000 S4000 M3

N70 G722 I0 J0 <RIN=40> <RFI=20> <QIN=0> <QFI=-10> <DPA=2> <ROT=2> <%FON=1>

N80 G0 Z50

M02

## G728 - Machining of 3D Surfaces obtained connecting two profiles that lie on parallel planes

## G726 - Definition of   parameters  and  first profile used by the G728 macro

## G727 - Definition of second profile used by the G728 macro

The G728  macro  allows to machine a lined 3D surface defined by 2  parallel profiles positioned at a given quotes.

The macro parameters  and the first involved profile  are programmed through the G726 associated  Function.

The second profile is instead defined through the G727 associated Function.

The working process  can manage    cylindrical, spherical and toroidal  tools.

The G728 macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

G726  Syntax:

G726 <XAT=..><YAT=..><QIN=..><DPA=..><DQS=..><QPO=..><KFE=..><DRA=..> ‘ Parameters Definition

L<PROF1>                                               					            ‘ First Profile definition

G727  Syntax:

G727   <QFO=..>

L<PROF2>                                                                                 		             ‘ Second  Profile definition

G728  Syntax:

G728                                                                                                                                    ‘ Machining start

DPA – Step definition [mm] along the first Profile.

QPO  - Detach quote, reached in Rapid in case of  mono directional machining.  If not programmed the milling will be bi-directional.

DQS  – Safety distance from which the movement  will restart at reduced working feed (F*KFE) re-attaching the profile.

KFE  -  Feed modifier coefficient applied on the start cutting movements  (default  KFE=1).

DRA – Surplus stock [mm]  that the working process will leave on the surface (default =0).

Notes:

- Both profiles (PROF1 and PROF2) can be defined using   ISO or GAP/EXPERT geometrical languages.  It is however suggested  to define them through two sub-routines .

- Both profiles  can be closed or open and can  contain an  unlimited  number of elements, but they must lie on 2 planes parallel to the defined Contouring Plane. They must include  also the attach/detach functions ( G41/G42/G47/G48   and G40 /G46).

- The contouring Plane can be eventually rotated through a dynamic array. The parameters QIN, QFO and QPO are however always referred  to the vertical axis.

- With the XAT and YAT  quotes is defined the starting point of the machining process. From this point the tool will go down, in rapid, to the quote QIN+DQS and so, at reduced  working feed  (F *KFE), will be reached   the QIN quote. As next step will be attached  the first  profile.

-  The first line will be the one linking the initial point of the first profile with the first point of the second profile.  The last line the one linking the last point of the first profile with the last point of the second profile.

- In case of  bi-directional milling (QPO parameter not programmed) the first line is executed at a reduced Feed (F*KFE) the next to the programmed Feed (F). The increment will be done alternatively on the first and on the second profile. On the first profile it will be always equal to DPA, while in the second  will be proportional to the ratio of the two profile lengths.

-  In case of mono-directional milling (QPO parameter defined) the working movement  is always  executed  from the first profile to the second one  at a reduced Feed (F*KFE), after this will be executed a rapid movement  on the vertical direction (orthogonal to the contouring plane) till the QPO quote is reached. Will follow:

- a movement, always in rapid, till the vertical to the starting point of the last done line is reached,

- a vertical movement, at rapid Feed, at the quote QIN+DQS,

- a vertical movement, at reduced working Feed (F*KFE) on the first profile,

- the execution of a DPA increment,

- the working of the next line at the programmed Feed (F).

Programming Example:

%

N0 G16XYZ+                                                          ‘Contouring Plane definition

N10 M6 T13                                                            ‘ Toroidal Milling Tool with  10 mm of Diameter

N20 M3 S2000 F500

N30 G0 Z15

N40 X0 Y0

N50 G726 <QIN=10><DPA=3><KFE=0.5><DQS=3><DRA:0>

N60 L<BOUNDARY>                                          ‘First  Profile definition

N70 G727  <QFO=5>

N80 L<HOLE>                                                     ‘Second Profile definition

N90 G728                                                               ‘Machining start

N100 G0 Z50

N110 X0Y0

N120 M02

“BOUNDARY” Sub Program

N10 G1 X0 Y-50 G42

N20 X-50 RA20

N30 Y50 RA20

N40 X50 RA20

N50 Y-50 RA20

N60 X0

N70 X0 Y0 G40

N80 <RET>

“HOLE” Sub Program

N10 G1 X0 Y-10 G42

N20 G2 I0 J0 X0 Y-10

N30 G1 X0 Y0 G40

N40 <RET>

## G738 - Machining of 3D Surfaces obtained by a “flat” profile and one or more “section” profiles

## G736 - Definition of   parameters  and  flat profile used by the G738 macro

## G737 - Definition of “section” profiles used by the G738 macro

The G738 macro allows to machine a 3D surface obtained moving a “Flat” profile along one or more “Section” profiles (till a maximum of  9).

The macro parameters  and the “Flat”  profile  are programmed through the G736 associated  Function.

The “Section”  profiles are  instead defined through the G737 associated Function.

The G738 macro Data Entry is activated, in MDI and Edit modes, through this keys sequence:

G736  Syntax:

‘ Parameters Definition

G736  <XAT=..><YAT=..><%RAC=..><%PAS=..><QPO=..><DQS=..><KFE=..><DRA=..><KRU=..><AAT=..>

L<FLAT>                                                                                              ‘Flat Profile definition

G737  Syntax:

G737

L<SECTION1>                                                                                      ‘Section 1 Profile definition

……

G737

L<SECTION9>                                                                                      ‘Section 9 Profile definition

G738  Syntax:

G738     <DPA=..>                                                                                  ‘Machining start

%PAS  – Type of machining :

%PAS=1 ( Mono directional machining  (default).

%PAS=2 ( Bi  directional machining.

QPO  - Detach quote, reached in Rapid in case of  mono directional machining.  If not programmed the milling will be bi-directional.

DQS  – Safety distance from which the movement  will restart at reduced working feed (F*KFE) re-attaching the profile.

KFE  -  Feed modifier coefficient applied on the start cutting movements  (default  KFE=1).

DRA – Surplus stock [mm]  that the working process will leave on the surface.

DPA – Distance (Pitch)  [mm] between two contiguous steps, measured  on the first “Section” profile

Notes:

- Programming  the “Flat” profile have to be respected the following rules:

It can be defined using ISO or GAP/EXPERT geometrical languages.

It is  suggested  to define it  through a  sub-routine.

It  can be independently  closed or open but  the number of  its elements cannot exceed 100.

It must lie on  the Contouring Plane that can  be eventually rotated through a dynamic array. The parameters  QPO and DQS are  however always referred  to the vertical axis.

It must include  the attach/detach commands that can be both  standard or tangential  (G41/G42/G47/G48 and G40 /G46).

When  programming  a “Flat”  profile where  will be applied  n ” Section”  profiles, it is necessary  to  define the portion of it, associated to the various sections. To do this it is necessary to use   the <SEZ:n> (with "n" from 1 to 9) instruction. The <SEZ:..> is positional  so it is effective starting from the current element until a new section is called through a new <SEZ:..>. As default, at the “Flat” profile beginning, is assumed active <SEZ:1>.

-  Programming  a “Section” profile have instead to be respected the following rules:

- It can be defined using   ISO or GAP/EXPERT geometrical languages and must be arranged as a Sub Program (L<…>).

- Every  “Section” profile requires a G737  function  that must be inserted  in a block alone before the call of the profile Sub Program.

- A number (from 1 to 9) is associated to every “Section” profile  on the basis of the position that  it takes  in the sequence of the G737. This number is the same   that must be written in the instructions <SEZ=n> of the “Flat”  profile.

The “Section” profile must be programmed on the same contouring plane used for the definition of the “Flat”  profile and must be an open profile.

The axis of the positive ordinate (Y in case of  contouring plane defined through G16XYZ+) must coincide with the positive perpendicular axis of the machine (Z in case of  contouring plane defined through G16XYZ +).

The profile has to include  the Attach / Detach. The use of  tangential  instructions G47/G48/G46 are however here not allowed (it generates a specific alarm).

In case of more “Section” profiles have to be defined, all their starting and ending points must have the same Y quotes. This also taking care of the Tool Radius compensation.

Programming Example (with 3 “Section” profiles):

%

N10 G16XYZ+

N20 M6 T10                                                                               ‘     Toroidal Tool with 20 mm of diameter

N30 M3 S2000 F500

N40 G0 X0 Y50 Z100

N50 G736 <%RAC=2><KFE=0.5><DRA:0>                         ‘     Parameters definitions

N60 L<PROFP>                                                                         ‘    “Flat “ profile definition

N70 G737

N80 L<PROFS1>                                                                       ‘    “ Section 1 “ profile definition

N90 G737

N100 L<PROFS2>                                                                    ‘   “ Section 2 “ profile definition

N110 G737

N120 L<PROFS3>                                                                    ‘   “ Section 3 “ profile definition

N130 G738 <DPA=2>                                                                ‘  Start machining with  Pitch  of 2 mm

N140 G0 Z100

N150 M02

“Flat ” profile  -    PROFP  Sub Program

N10 G1 X0 Y-300 G48

N20 G1 X-500 RA115

N40 G1X-350 Y250 RA80 <SEZ:2>

N50 X350 RA80 <SEZ:3>

N60 Y-300 X500 RA115 <SEZ:2>

N70 X0 <SEZ:1>

N80 Y-200 G46

N90 <RET>

“Section 1”  profile  - PROFS1 Sub Program

N10 G1 X0 Y200 G41

N20 G1 RC0

N30 G3 I210 J200 X210 Y0

N40 G1 X250

N50 G1 X260 G40

N60  <RET>

“Section 2”  profile – PROFS2 Sub Program

N10 G1 X0 Y200 G41

N20 X10

N30 G1

N40 G3 I110 J100 X110 Y0

N50 G1 X120 Y0

N60 X500 G40

N70 <RET>

“Section 3”  profile – PROFS3 Sub Program

N10 G1 X0 Y200 G41

N20 X30 RA20

N30 Y0 RA50

N40 X90

N50 X300 G40

N60 <RET>

# Macros repetitions on Lines / Arrays

L<FORFLA> - Execution of Canned Cycles / Macros on a Arc of Circle

The “FORFLA macro can be used to execute a group of contiguous working process, positioned, with a constant angular pass, along an arc. Using the “FORFLA” macro, it is possible to carry out the fixed cycles from G81 to G89, as well as the macros G88, G188, G189, G185, G186, G190 and the cycle G184. The macro can be programmed in two different ways in base to the set parameters. Parameters common to both programming method: I.. J.. – Coordinates of the centre of the Arc. %NHL – Number of working process to be executed). ARC - Position modality. ARC=0 Movement between to contiguous point done in Rapid (G00). ARC=1 Movement along the Arc (G02/G03) Method 1 - Defining the co-ordinates of the initial cycle application point, the centre of the arc and the angle associated to the last point. The Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: L<FORFLA> X.. Y.. I.. J.. <%NHL=..> <ARC=..> <RDF=0> <AIN=..> Method 2 - Defining the radius and centre of the arc and the angle associated to the first point. The Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: L<FORFLA> I.. J.. <%NHL=..> <ARC=..> <RDF=..> <ANA=..> Notes: - To avoid undesired behaviors it is necessary, before to use this macro, to initialize properly all parameters, also those not used. - The above used syntax assumes that XY has been defined as Contouring Plane. In case of different designation, also the Circle Center co-ordinates will change coherently. For example in case of Contouring Plane XZ they will change from I.. J.. to I.. K..

L<FORMAT> - Execution of Canned Cycles / Macros on an Array

The macro “FORMAT is used to execute a group of working process arranged at constant pitch along the lines of an array. Using the “FORMAT” macro, it is possible to carry out all fixed cycles from G81 to G89, as well as all macros G88, G188, G189, G185, G186, G190 and the solid tapping cycle G184. The Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: L<FORMAT> X.. Y.. <%NHL=..> <%NRG=..> <PXL=..> <PYL=..> <PXR=..><PYR=..> FORMAT used to program a generic number of aligned working process . In this case the Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: L<FORMAT> X.. Y.. <%NHL=..> <%NRG=0> <PXL=..> <PYL=..> Note: During execution of the FORFLA or FORMAT cycles it is possible to display on the CNC Operator Panel the values of %NHL and %NRG (only for macro FORMAT) parameters . This is useful if machining is resumed after is has been interrupted for accidental reasons, during the macro FORFLA or FORMAT. To know in details as to proceed in this situation see chapter 16 of “Milling Machine User’s Manual” ECS code 721P392.

L<WRITE> - Engraving of a String of Characters

The Macro <WRITE> is used to engrave strings composed by alphanumeric characters. Strings can be freely positioned. Characters representation is proportional type ( no fixed width). Of course it is possible to select Upper or Lower case, Italics or Standard style, desired character size (expressed as height/width ratio). In this case the Data Entry is activated, in MDI and Edit modes, through this keys sequence: Syntax: L<WRITE> X… Y… <STR:”String of characters and symbols”> <RIN=...> <DAX=...> <DAY=...> <AIN=...> <FE1=...> <FE2=...> <FE3=...> <RAP=…> <ENT=…> <RAL=…> Parameters description: X.. Y.. - Coordinate of the bottom left corner of the first character of the string to be engraved. <STR:”……”> Is the string of characters to be engraved. It can contain up to 39 characters. The string must be written between “inverted commas”. Are accepted the following character’s set: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F,G,H,I,J,K,L,M,N,O,P,Q,R,S,T,U,V,X,Y,W,Z,a,b,c,d,e,f,g,h,i,j,k,l,m,n,o,p,q,r,s,t,u,v,x,y,w,z, “space”, ‘, (, ), *, “comma”, “dot”, +, -, /, DAX /DAY - Width / Height of the character [mm]. Selecting the Height it is important to verify that the Height / Width ratio stays inside the range 0.8 – 2. AIN – Character inclination [°]. Are accepted values in the range 0 - 15°. FE1 – Engraving Feed [mm/min] FE2 – Feed of the vertical axis to return to an already engraved quote [mm/ min] . Typically applied during engraving the char baseline (for example the horizontal segment of number “1”). FE3 – Cutting penetration of the vertical axis applied between RAP and ENT quote [mm/min] RAP / ENT / RAL – Same meaning as for Canned Cycles.

# Static and Dynamic Matrices

Static and Dynamic Matrices - Basic concepts

A transformation matrix consists of an array of numbers (matrix coefficients) arranged in a table of three rows, each row being made up of four coefficients. a11 a12 a13 a14 a21 a22 a23 a24 a31 a32 a33 a34 where: Zl, Xl, Ql - Represent the coordinates of a point to be transformed, i.e. those in the part program which are to be translated, rotated, and so on. They are the coordinates of a so-called local system. Zb, Xb, Qb- Represent the coordinates of the point transformed by the matrix, i.e. the result of the transformation. The ECS CNCs allow the programming of two distinct types of matrices: Static matrices. These matrices are only applied at interpreter level, therefore they only act on the initial point and end point of each element in the profile. In other words Static Matrices can transform points (G0 and G1) both in a plane and in the space, while arcs of a circle can only be transformed in planes perpendicular to the programmed planes. Dynamic matrices. These are applied at interpolator level, allowing transformations of arcs of circles with any orientation in the space. Note: Whenever a Static and a Dynamic Matrix are simultaneously active it is necessary that the axes upon which they act are either the same or totally different.

Static Matrices Programming

To program in a Part program a static transformation matrix, it is necessary to use the following instructions: <MAT: name; matrix coefficients> Which assigns a name to the static matrix and defines its associated parameters. <MTX: first axis, second axis; third axis> - Which specifies the axes involved in the transformation. <TCT: ON; name> - That enables the static transformation associated to the matrix identified with “name”. <TCT:OFF> - That disable the static transformation matrix currently active. <MAT: OFF; name> - That cancels the previously defined static matrix. Notes: The 12 matrix coefficients can be defined as R variables or more generally as expressions. The matrix name can be composed by max. 6 alphanumeric characters. The ECS CNCs can memorize up to 5 static matrices however only one at time can be enabled. The matrices stored do not affect programs, unless they are enabled by instruction <TCT:ON;….> All static matrices are deleted in the case of CNC Reset, Mode changes and Initialization of a new program (%). Example of matrix definition/activation …… N.. <MAT:TRASL; 1; 0; 0; 230; 0; 1; 0; 150; 0; 0; 1; 0> N.. <MTX:X;Y;Z> N.. <TCT:ON;TRASL> ……

L<TRANS> - Single / Multiple Translation Static Matrix

This matrix allows to translate a profile, described with a sequence of geometrical instructions, by a configurable quantity X, Y, Z along the homonymous axes. It allows also to repeat the operation a desired number of time. The Data Entry associated to this functions, in Edit and MDI, can be activated by the sequence of keys: Syntax: <%CON=1> L<TRANS> <DTX=…> <DTY=…> <DTZ=…> <%NPR=…> Where: DTX – translation [expressed in mm] along the first axis declared into the <MTX: …> instruction ( typically X). DTY – translation [expressed in mm] along the second axis declared into the <MTX: …> instruction ( typically Y). DTZ – translation [expressed in mm] along the third axis declared into the <MTX: …> instruction ( typically Z). %NPR - number of desired repetitions ( used by <RPT:…> block). %CON – Repetition counter. Must be initialized to 1 before the L<TRANS> call and forced again =1 at the end of the repetition loop. Programming example: % N10<MTX:X;Y;Z> <%CON=1> ... N100 L <TRANS> <DTX = 180> <DTY=120> <DTZ=0> <%NRP=3> N120 <%CON=%CON+1> N130 <RPT:N10; N120;<%NRP>> N140 <TCT:OFF> <%CON=1>

L<ROTX> - Rotation around X axis

L<ROTY> - Rotation around Y axis

L<ROTZ> - Rotation around Z axis

L<ROTXYZ> - Rotation in sequence around XYZ axes

This matrixes allows to apply, to a profile described with a sequence of geometrical instructions, a rotation of a defined angle around a programmed axes . It allows also to define how many time the rotation should be executed. The Data Entry associated to this function, in Edit and MDI, can be activated by the sequence of keys: Syntax: L<ROTX > <ANR=…> L<ROTY> <ANR=…> L<ROTZ> <ANR=…> L<ROTXYZ> <ANR=…> <AN2=…> <AN3=…> Where the parameters ANR, AN2 and AN3 represent : <ANR=…> the angle of rotation, expressed in °, applied around the X, Y or Z axes, or more generically around the first axis declared on the associated <MTX:….> instruction. <AN2=…> the angle of rotation, expressed in °, applied around the Y axis, or more generically the second axis declared on the associated <MTX:…> instruction. <AN3=…> the angle of rotation, expressed in °, applied around the Z axis, or more generically the third axis declared on the associated <MTX:…> instruction. Note: The value associated to variables ANR, AN2 and AN3 is negative in case of anti clockwise rotation, is instead positive in case of clockwise rotation.

L<ROTRAS> - Repetition with Roto-translation Static Matrix

This matrix allows to apply, to a profile described with a sequence of geometrical instructions: - a rotation of a specified angle around a defined point. - a translation of the obtained profile of X, Y,Z along the homonymous axes. It allows also to define how many time to execute the above described roto-translation. The Data Entry associated to this function, in Edit and MDI, can be activated by the sequence of keys: Syntax: L<ROTRAS> <XCE=…> <YCE=…> <ANR=…> <DTX=…> <DTY=…><%NRP=…> Programming Example: % N0 <MTX:X;Y;Z> N10 T3 M6 N20 S500 F200 N30 L<ROTRAS><ANR=35> <DTX=215> <DTY=125><XCE=0><YCE=0><%NRP=1> N40 G16 XYZ+ N50 X50 Y100 M13 N60 Z3 N70 G01 Z-20 N80 G41 X0 Y100 N90 X0Y0 N100 X200 N110 G03 X200 Y100 I200 J50 N120 G01 X100 N130 Y200 N140 G03 X0 Y200 I50 J200 N150 G01 Y100 N160 G40 X50 Y100 N170 G00 Z100 M05 N180 <TCT: OFF> N190 M2

L<SCALE> - Change Scale Ratio Static Matrix

This matrix allows to apply, to a profile described with a sequence of geometrical instructions, a desired scale factor. The Data Entry associated to this function, in Edit and MDI, can be activated by the sequence of keys: Syntax: L<SCALE> <SCA=…> Where : SCA = Multiplier Scale factor

Dynamic Matrices Programming

To program in a Part program a dynamic transformation matrix it is necessary to use the following instructions: <MAT: name; matrix coefficients> - Which assigns to the dynamic matrix a name and define its associated parameters. <DMX: first axis, second axis; third axis> - Which specifies the axes involved in the dynamic transformation . <DCT: ON; name> - That enables the dynamic transformations associated to the matrix identified with “name”. <DCT:OFF> - That disable the dynamic transformation matrix currently active. <MAT: OFF; name> - That cancels the previously defined dynamic matrix. Notes: The 12 matrix coefficients can be defined as R variables or more generally as expressions. The matrix name can be composed by max. 6 alphanumeric characters. The ECS CNCs can memorize up to 5 dynamic matrices however only one at time can be enabled. The matrices stored do not affect programs, unless they are enabled by the instruction <DCT:ON;….> CNC RESET, mode change and Program Start %, that cancel Static Matrices, do not affect the dynamic ones, which can therefore be defined as “super-modal”.

L<TRACYIL> - Cylindrical Programming - Dynamic Matrix

The TRACYL dynamic matrix allows to machine a profile programmed into the virtual Cartesian plane Y -B on a surface of a cylinder. The matrix will provide to compute automatically the correspondent values of the B angles. A typical examples of these workings are channel-type cylindrical cams and drum cams. To program a cylindrical cam it is in fact normally available a plan drawing of the cam, with the abscissa represented by the B rotary axis (quoted in millimeters) and the ordinate standing for the longitudinal Y axis (also quoted in mm). Data Entry associated to this function, in Edit and MDI, can be activated by the sequence of keys: Note: Into the instruction <DMX: Axis1;Axis2 ;Axis3> as “Axis1” must be defined the Rotative axis, while as “Axis2” the linked linear axis, finally as “Axis3” must be declared the depth axis. With reference to the above figure it will be: <DMX:B;Y;Z>. Programming Example: % N0 G16BYZ+ ‘ Definition of the Contouring Plane BY N10 <DMX:B;Y;Z> ‘ Definition of the axes involved in the trasformation N20 T2 M6 N30 S800 M13 N40 L<TRACYL> <DIA=382> N45 X0 N50 Y110 Z220 B0 ‘ Definition of the initial point N60 G1 Z191 F150 N70 G42 B0 Y120 N80 B250 Y120 RA50 ‘ Definition of the came profile into the virtual Cartesian plane YB N90 B600 Y300 RA60 N100 B850 RA60 N110 Y120 RA18 N120 B1200.09 N130 G0 G40 B1200.09 Y110 N140 Z220 M5 N150 <DCT:OFF> ‘ Transformation (TRACYL Matrix) disabling N160 M2

L<DROTX> - Rotation of the Contouring Plane around the first DMX Axis

L<DROTY> - Rotation of the Contouring Plane around the second DMX Axis

L<DROTX> - Rotation of the Contouring Plane around the third DMX Axis

L<DROTX> - Multiple rotation of the Contouring Plane around the DMX Axes

The DROTX, DROTY, DROTZ and DROTXYZ dynamic matrix allows to rotate a profile programmed on the defined Contouring Plane around one or more axes but they are typically used to execute Macros or Canned Cycles on inclined plan. Of course these kinds of operation requires a machine equipped with a mono/bi-rotative head able to physically carry the tool orthogonal to the inclined working plane. The Data Entry associated to this function, in Edit and MDI, can be activated by the sequence of keys: Syntax: L<DROTX > <ANR=…> L<DROTY> <ANR=…> L<DROTZ> <ANR=…> L<DROTXYZ> <ANR=…> <AN2=…> <AN3=…> Where the parameters ANR, AN2 and AN3 represent : <ANR=…> the angle of rotation, expressed in °, applied around the X, Y or Z axes, or more generically around the first axis declared on the associated <DMX:….> instruction. <AN2=…> the angle of rotation, expressed in °, applied around the Y axis, or more generically the second axis declared on the associated <DMX:…> instruction. <AN3=…> the angle of rotation, expressed in °, applied around the Z axis, or more generically the third axis declared on the associated <DMX:…> instruction. Notes: The value associated to variables ANR, AN2 and AN3 is negative in case of anti clockwise rotation, is instead positive in case of clockwise rotation. The DROTX, DROTY, DROTZ and DROTXYZ dynamic matrix operate around the origin. If it is necessary a roto- translation it is necessary to use the G59... instruction. If a mono/bi-rotative head is used, to compensate all the mechanical offset is enough to issue the G51 instruction.

# Measuring Cycles with Probe

Measurement Cycles General Considerations

The available measuring cycles need an ON/OFF-type Probes mounted on the spindle or on the machine table in a fixed position. They allow to: - Perform a dimensional check of the machined work piece measuring the errors between the measured dimensions and the programmed ones. - Correct tool Length and Radius (L and R) change their values in the Tool Table. - Correct the axis zero point (Origin) and change their values in the CNC Origins Table. - To pre-set or check the tool length by means of a probe mounted in a fixed position. Notes: Both types of probes -on the spindle and in a fixed position - can be present at the same time on the machine. The above-mentioned corrections in some cases are executed automatically, whereas in other cases they are subject to confirmation from the operator . In addition, by comparing the measured error to the programmed tolerance, a series of messages addressed to the operator are displayed. The test procedures can be used either by directly inputting them in the machining cycle written for the work-piece or calling them as subroutines with instruction L<subroutine name>. It is possible to specify more than one test program in the same Part Program. Measuring cycles must always be executed in G94 mode (i.e. F = mm/min) and with the spindle still.

Measurement Cycles General Parameters & Definitions

Nominal Coordinate It is the dimension specified on the drawing used to write the work piece Part Program. Measurement Coordinate – Are the coordinates of the theoretical point at which an axis has to be positioned in order to measure the coordinate itself. They must be defined taking in consideration the max tolerance accepted for every dimensions. For example the drawing quote 100-0+0.024 becomes 100.012 as Measurement coordinate. Wide Tolerance LTZ -It is the max. deviation from the Measurement Coordinate accepted by the CNC when correcting the factor that caused the error. For example if <LTZ=0.5> is programmed, it means that the factor that caused the error (tool or origin), will be corrected by a max. value of ( 0.5 mm. The Wide Tolerance must therefore be higher than the expected measurement error on the work piece. If during a measuring cycle is detected an error higher than the value attributed to LTZ, a message will be displayed on the screen asking the operator whether he wants to continue with the measuring cycle or not. During a Measurement cycle the CNC brings the axes at rapid feed-rate to the coordinate given by: Measurement coordinate - 2*(LTZ+0.5). Close Tolerance STZ - It is the deviation from the Measurement Coordinate which does not cause the CNC to make any correction involving the factor “responsible” for the error. For example <STZ=0.02> means that if an error of less than 0.02 mm is found on the Measurement coordinate, no correction will be made. Notes: STZ must always be smaller than LTZ. STZ=0 means that the factor that caused an error will always be corrected, even if the error is negligible. Is better to program STZ #0 to avoid making very slight corrections to tools or origins.

Measurement Cycle Preparatory Parameters & Instructions

Before start a Measurement Cycle it is necessary to define: The Contouring Plane (through G16..., G17, G18 or G19 instructions). The vertical axis where will be applied the Canned Cycles (through <CFF=CF..> instruction). The vertical quote reached in rapid by the probe (<RAP=..>). The vertical quote reached by the probe at a reduced Feed of 3000 mm/min (<ENT=..>). The vertical quote where will be positioned the probe, in rapid, at the measurement cycle end (<RAL=..>). <MIS=a.b> - Specifies the type of measurement to be carried out. a= 0 measurement without correction (errors are only displayed) a= 1 measurement with correction of the responsible factor. a= 2 no measurement but utilization of the date detected in foregoing measurement cycles. b= 0 the measure have not be modified taking care of the probe misalignment . b= 1 the measure will be modified taking care of the probe misalignment. Example : <MIS=1.1 > means: Measurement with correction taking care of the probe disalignment. <TYP=yyy.x> - Specifies the type of correction and the factor responsible for the error x=0 Origin correction x=1 Tool Radius correction (or Radius offset). x=2 Tool Length correction (or Length offset) yyy Number of the factor responsible for the error (max. 3 digits) The responsible factor yyy can be programmed with positive or negative sign according to the type of correction selected: It will be positive in case we desire to correct Origins or Tool. It will be negative when instead we want to correct the Probe Radius. Examples: <TYP=-15.1> Correction of the length of tool T15 (the “-” sign indicates that the tool 15 is the Probe). <TYP=17.0> Correction of Origin no. 17 <TYP=13.1> Correction of the Radius of tool T13. <TYP=15.2> Correction of the Length of tool T15. <ROT=..> Spindle Orientation. If <ROT=0> the spindle isn’t oriented. If <ROT=1> the measurement will be done with the spindle oriented. F… Feed in mm/min that will be maintained moving the probe during the measurement. L<TESTON> Initialization of a Measurement cycle. It has to be programmed before starting one or more test cycles. It forces the following conditions: F300, <LTZ=0.05>, <STZ=0.01>, <ROT=0> L<TESTOF> End of the Test cycles. It must be programmed at the end of one or of a series of measuring cycles.

G201 - Single Movement - Measurement Cycle

This cycle is useful to check and - if required - to correct an error found on a machined work piece .It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G201 X.. Y.. <DAX=..><DAY=..><RAL><RAP><ENT><MIS=..><TYP=..> F.. DAX - Distance between the measurement starting point and the point to be measured along the first axis of the Contouring Plane (X in case the C.P is defined with G16XYZ+ or G17 ). DAY - Distance between the measurement starting point and the point to be measured along the second axis of the Contouring Plane (Y in case the C.P. is defined with G16XYZ+ or G17). Note: The G201 is a modal instruction so must be cancelled through the G200 function (see).

G202 - Two Internal Movements - Measurement Cycle

This cycle is useful to measure pocket with parallel surfaces ( check and - if required - to correct an error found ).It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G202 X.. Y.. <DAX=..><DAY=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F.. DAX - Distance between the measurement starting point and the point to be measured along the first axis of the Contouring Plane (X in case the C.P is defined with G16XYZ+ or G17 ). DAY - Distance between the measurement starting point and the point to be measured along the second axis of the Contouring Plane (Y in case the C.P. is defined with G16XYZ+ or G17). Note: The G202 is a modal instruction so must be cancelled through the G200 function (see).

G203 - Two External Movements - Measurement Cycle

This cycle is useful to measure solids with parallel surfaces (check and - if required - to correct an error found ).It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G203 X.. Y.. <DAX=..><DAY=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F.. Note: The G203 is a modal instruction so must be cancelled through the G200 function (see).

G204 - Four Internal Movements - Measurement Cycle

This cycle is useful to measure a diameter of a circular holes ( check and - if required - to correct an error found ).It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) It commands the execution of four movements with a phase increment of 90° . The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G204 X.. Y.. <DIA=..><AIN=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F.. Notes: The G204 is a modal instruction so must be cancelled through the G200 function (see). When using this measurement cycle, it is useful before to qualify the probe using a measurement cycle G204 attributing the error to the probe itself through the instruction <TYP=-....>. If the probe has also a different sensitivity on the commutation in 4 directions, it is necessary to set, for both the probe qualification and the measurement cycle, the variable <ROT=1> that guarantee the same orientation during both operation.

G205 - Four External Movements - Measurement Cycle

This cycle is useful to measure the diameter of a cylinder ( check and - if required - to correct an error found ).It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) It commands the execution of four movements with a phase increment of 90° . The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G205 X.. Y.. <DIA=..><AIN=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F.. Notes: Same notes valid for G204 Measurement Cycle.

G206 - Three Internal Movements - Measurement Cycle

This cycle is useful to measure the diameter of a generic arc of circle engraved on flat surface. It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) It commands the execution of three movements defining the angle of the first one and the increment to be applied to obtain the next two. The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G206 X.. Y.. <DIA=..><AIN=..><ANA=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F. Notes: The G206 is a modal instruction so must be cancelled through the G200 function (see). When using this measurement cycle, it is useful before to qualify the probe using a measurement cycle G204 attributing the error to the probe itself through the instruction <TYP=-....>. If the probe has also a different sensitivity on the commutation in 4 directions, it is necessary to set, for both the probe qualification and the measurement cycle, the variable <ROT=1> that guarantee the same orientation during both operation.

G207 - Three External Movements - Measurement Cycle

This cycle is useful to measure the diameter of a generic arc of circle on relief on a flat surface. It is possible to correct the following responsible factors: Origins / Tool Length (L) and Radius (R) It commands the execution of three movements defining the angle of the first one and the increment to be applied to obtain the next two. The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G207 X.. Y.. <DIA=..><AIN=..><ANA=..><RAL><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..><ROT=..> F. Notes: Same notes valid for G206 Measurement Cycle.

G208 - Three External Movements - Measurement Cycle

This cycle is useful to align a part on a rotational table applying a correction to the Origin associated to the table. It commands the execution of two movements defining the distance between them. The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G207 X.. Y.. <DAX=..><DAY=..><AXS=CF.><RAL ><RAP><ENT><MIS=..><TYP=..><LTZ=..><STZ=..>F.. Notes: The G208 is a modal instruction so must be cancelled through the G200 function (see). It is suggested that the positioning error to be corrected never exceed ( 30° (with reference to the first axis of the C.P.)

G210 - Probe Qualification Cycle

This cycle allows to measure the Probe rod misalignment error when it is in idle condition. The error is detected along the 2 axes of the configured Contouring Plane. And need to program twice the cycle ( see, for details, next example) The errors will be saved on two CNC’s system variables (#113 and #114 ) that will be used by the other cycles to correct measurements. To activate this compensation, it is necessary to put b=1 into the instruction <MIS=a.b>. The cycle requires a gauge block mounted on the surface of the Tool Machine and that the programming origin is done with the maximum precision on the centre of the gauge block. The Data Entry associated to the G210 cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G211 X.. Y... <DAX=...><DAY=...><ENT=...><RAL=...><RAP=...> <MIS=...> F.. DAX – Distance, measured along the first axis on the contouring surface (X in the case we define the C.P. with of G16 XYZ+ or G17), between the measurement starting point (P1/P2) and the probe “contact point” on the gauge block . DAY– Distance, measured along the second axis on the contouring surface (Y in the case we define the C.P. with of G16 XYZ+ or G17), between the measurement starting point (P1/P2) and the probe “contact point” on the gauge block. Programming Example: We want to detect the probe rod misalignment along the X and Y axes (Ex and Ey respectively) using a 20x20 gauge block mounted on the surface of the Tool Machine. As preliminary job the origin N.9 will be formed with the maximum precision on the centre of the gauge block. The Measurement program so should be the following: .... T20 M06 ‘ We assume T20 the probe to be qualified G16 XYZ+ <CFF=CFZ> G54.09 M28 ‘ Probe activation L<TESTON> ‘ Measurement Cycle inizialization M19 ‘ Spindle Orientation <LTZ=0.5> <STZ=0> F300 ‘ First measurement G210 X-20 Y0<DAX=10><DAY=0><RAP=-10><ENT=-10> <RAL=20> <MIS=2.9> ‘ Second measurement X0 Y-20 <DAX=0><DAY=10> ‘ Cancel measurement cycles G200 L<TESTOF> M29 ‘ Probe de-activation ....

G211 - Measurement Cycle with Probe in fixed position

A probe mounted in a fixed position of the machine tool can be used to automatically pre-set the tool lengths, or check that the tool is in good conditions. The Data Entry associated to this cycle can be activated, in Edit and MDI, by the following sequence of keys: Syntax: G211 X.. Z... <DAX=...> <MIS=...> <TYP=...> Notes: The G211 is a modal instruction so must be cancelled through the G200 function (see). As default the correction will be applied to the tool mounted on the spindle.

G200 - Cancels Measurement Cycle

The G201…..G211 Measurement Cycles are modal instructions so, at the end of the test they must be cancelled through the G200 function.

Measurement Cycles - Results Data Collection

At the end of every measurements cycle a message, resuming the results of the operation, is carried out on the screen and the related correction applied (programming at the and of the measurement cycle an M00 or M01 function the message will remain on the screen till the operator don’t decide to press Start). It is however possible to store the results of the measurements in a file for later analysis. The memorization is managed through the following instructions: <PRT=0> Memorization disabled. It will be programmed at the end of the measuring cycle or whenever we want to disable the results memorization into a file. <PRT=2> Creation of the file TESTDAT.TAB containing the results of the measurements (up to 100). This file is saved in the C:\ECS.CNC\TAR directory. If we wish to print out its contents, it is recommended to export the file (using the Output function) into a personal computer where is installed Microsoft EXCEL® and utilize this program to reorganize/process the data. A description of the various data fields present in TESTDAT.TAB is available in the file TESTDAT.TXT, which is also located in C:\ECS.CNC\TAR folder. Note: Among the data saved in the file TESTDAT.TAB is included the value taken from the integer variable %COD, which the programmer may appropriately initialize prior to each cycle in order to use it as a generic discriminating element.

Measurement Cycles - Programming Examples

1) G203 Example Measurement of a distance (P2-P3) between the two sides of a parallelepiped and compensation of the error modifying the tool radius ... N100 G16XYZ+ <CFF=CFZ> N110 T20 M6 N120 M... ‘ Probe Switch on N130 L<TESTON> ‘Measurement Cycles initialization N140 <PRT=2> ‘Start measurement results storing N150 <ROT=1> ‘Spindle orientation N160 <LTZ=...> <STZ=...> ‘Define Large and Narrow Tolerances N170 G203 X0 Y0 <ENT=-20><RAP=10><RAL=100> <MIS=1.0><TYP=1.0><DAX=50><DAY=0>F50 N180 X0 Y0 <MIS=2.0><TYP=12.1> N190 G200 ‘ Measurement cycle G203 de-activation N200 L<TESTOF> ‘ Restore parameters N210 <PRT=0> ‘Stop measurement result storing N220 M... ‘ Probe Switch off ……. Comments to line N170 The G203 measurement cycle is carried out with error correction without take care of the probe misalignment (<MIS=1.0>), the correction is applied the Origin N.1 (<TYP=1.0>). A 50mm segment of both sides of the parallelepiped (<DAX=50>) is measured. The probe approaches the piece with a Feed of 50 mm/min (F50). Comments to line N180 In this block isn’t done a measurement but the assignment of the foregoing detected error as a radius offset on the T12 Tool (<MIS=2.0> <TYP=12.1>). Note that, because G203 is modal, it isn’t necessary to reprogram it, but only specify the starting measurement point.(X0 Y0). 2) G204 Example We want to show the value of the diameter and the oval shape of a hole using measurement cycle G204 on four internal points. As consequence tool radius and the origins of the centre of the programmed circle will be corrected. ... N100 G16 XYZ+ <CFF=CFZ> N110 T20 M6 N120 M... ‘Probe switch On N130 L<TESTON> ‘Measurement Cycles initialization N140 <PRT=2> ‘Start measurement results storing N150 <ROT=1> ‘Spindle Orientation N160 <LTZ=1><STZ=0> ‘Define Large and Narrow tolerances N170 G204 X0 Y0 <ENT=-10> <RAP=-10> <RAL=100> <MIS=1.0><TYP=2.0> <DIA=100> <AIN=80> F50 N180 X0 Y0 <MIS=2.0><TYP=13.1> N190 G200 ‘ Measurement cycle G204 de-activation N200 L<TESTOF> ‘ Restore Parameters N210 <PRT=0> ‘ Stop measurement result storing N220 M... ‘ Probe switch Off ... Comments to line N170 The G204 measurement cycle is carried out with error correction without take care of the probe misalignment (<MIS=1.0>), the correction is applied the Origin N.2 (<TYP=2.0>). The internal measurement cycle on 4 points is carried out, the first at 80° (with reference to X axis), the second at 170°, the third at 260° and the fourth at 350°.Every time a segment of 50 mm of radius is measured (<DIA=100>). The probe approaches the piece with a Feed of 50 mm/min (F50). Comments to line N180 In this block isn’t done a measurement but the assignment of the foregoing detected error as a radius offset on the T13 Tool ( <MIS=2.0> <TYP=13.1>). Note that, because G204 is modal, it isn’t necessary to reprogram it, but only specify the starting measurement point. ( X0 Y0 ). 3) G206 Example Through a G206 cycle we want to measure the errors on the center and on the radius of the relief arc and assign them respectively to the Origin N. 1 and at the Radius of the tool T11. ... N100 G16 XYZ+ <CFF=CFZ> N110 T20 M6 N120 M... ‘ Probe switch On N130 L<TESTON> ‘ Measurement Cycles initialization N140 <PRT=2> ‘ Start measurement results storing N150 <LTZ=1><STZ=0> ‘ Define Large and Narrow tolerances N160 <ROT=0> ‘ No spindle orientation N170 G206 X100 Y50 <RAP=-10> <ENT=-10> <RAL=100> <MIS=1.0> <TYP=1.0> <DIA=160> <AIN=60> <ANA=20> F50 N180 X100 Y50 <MIS=2.0><TYP=11.1> N190 G200 N200 L<TESTOF> ‘ Restore Parameters N210 <PRT=0> ‘ Stop measurement result storing N220 M... ‘ Probe Switch Off ... Comments to line N170 The G206 measurement cycle is carried out with error correction without take care of the probe misalignment (<MIS=1.0>). The measurement cycle on 3 points is carried out, the first at 60° (<AIN=60>), the second at 80° (60° + 20°( <ANA=20>), the third at 100° (80°+20°).So the calculated center is compared with the programmed one (X=100 and Y=50). The correction is applied to the Origin N.1 (<TYP=1.0>). Comments to line N180 In this block isn’t done a measurement but the assignment detected error on the radius as a radius offset on the T11 Tool (<MIS=2.0> <TYP=11.1>). Note that, because G206 is modal, it isn’t necessary to reprogram it, but only specify the starting measurement point. (X100 Y50).

Notes:

# Text boxes

G59 X30 Y80 Y30

X

Y

80

30

30

80

Y

X

G58 X30 Y80 RC30

30°

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Return  Quote reached at rapid

SPD –  Spindle Speed [rpm].

PCH -  Tapping  Pitch[mm].

ROT – Spindle sense of rotation

ROT = 3   clockwise rotation right side treading

ROT = 4   anticlockwise rot. Left side treading.

I   Xpole

P2

Pole

e

P2

P3

P2

P1

P

Y

X

P1

Y

YP2

J..

I..

P1

P2

XP2       X

G17

Element n

G40  K X… Y..

Element1

P1

Pend

Pini

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Return  Quote reached at rapid

SPD –  Spindle Speed [rpm].

PCH -  Tapping  Pitch [mm].

ROT – Spindle sense of rotation

ROT= 3 clockwise rotation right side treading

ROT = 4 anticlockwise rot. Left side treading

DAX – Radial release at the end of the Threading

a

Ypole

Xpole

X

Y

or  +

….

G0 X..Y..           ‘ Point P1

G42

X.. Y..                ‘ Point P2

X.. Y..                ‘ Point P3

…..

P1

Notes:

Before enabling the “WRITE” macro must be defined both  the Contouring Plane (G16… or G17, G18, G19)  and  the axis where to apply the  canned cycles (<CFF=CF..>).

If the “WRITE” macro is written in several P.P. blocks all the parameters associated must be previously defined

Specific Parameters of this  programming mode:

RDF – Is  the  Radius  of the Arc [mm]

ANA – Angle [°] between  X axis and First  point  It will be positive if measured in the anti-clockwise direction, negative otherwise.

AIN – Angle between two contiguous points.

Specific Parameters of this  programming mode:

X.. Y..  – Coordinates of the first cycle application point (P)

RDF – In this modality must be put equal to 0

AIN – Angle [°]  between Initial and Final point. It will be positive in case of anti-clockwise direction, negative otherwise.

3D Surface  obtained

“Section” Profiles

Flat  Profile

The example reported in the Figure shows a typical error that occur if we forget to take into account the offset introduced by the tool radius compensation.

In this case in fact, Section 1 and Section 2 look perfectly aligned ( with reference to Y axis).

But  machining the part with a Spherical or a Toroidal tool this is not more true. So, in this case the CNC will issue an alarm.

X

Section 2

P3

P2

Solution identified by K

G02 X.. Y.. R.. K

R..

R..

X..Y..

where:

X..  /Y.. – Abscissa and Ordinate of the arc  final point

I.. / J..   –  Abscissa and Ordinate of the center of the  arc

RC.. – Absolute angle of the arc  final point

RB .. – Relative angle of the arc final point

R.. – Arc Radius

K – used to differentiate the two possible solutions of this kind of definition (see figure).

where:

X.. – Abscissa of the line final point

Y.. – Ordinate of the line final point

RC.. – Absolute inclination (with reference to the first axis of the C.P.)

D.. – Line length

Element2

In this case the tool  moves on Element n till to arrive to be tangent to Element n+1 . At this point Tool compensation is forced OFF and the tool  reach point X… Z… with its  point.

Both Element n /  Element n+1  can be  Lines or Arcs  defined  in all possible ways  foreseen  by  ISO, GAP and EXPERT languages.

80

35

70

P3

30

….

N90    G0  X70 Y35                                   {P1}

N100 G48 <TGR: 3 ; 45> X30  Y80        {P2}

….

P2

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Return Quote reached at rapid

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Quote reached in rapid  at the end of  the cycle

TIM –   Dwell at the ENT quote [sec].

Parameters description:

ENT - Depth  quote

RAP - Quote reached in rapid at the beginning of cycle

RAL  -  Quote reached in rapid  at the end of  the cycle

SF1 /SF2 – Quotes used to define the 2 zones where the bit will change the Feed.

FE1 - Feed  [mm/min] used into the zone SF1

FE2 - Feed  [mm/min] used into the zone SF2

45°

%

N0    G16XYZ+

N10  T4 M6

N20  G0 X80 Y30 S..  F..                  {PINZ}

N30  Z-20 M3

N40  G48 X30 Y80                            {P1}

N50  G1 X60 Y110                            {P2}

N60  G2 I100 J70 X156.57 Y70        {P3}

N70  G1 Y0

N80  X0

N90  Y50

N100 X30 Y80                                    {P1}

N110 G0 G46 X80 Y30                      {PINZ}

N120 Z100 M5

N130 M2

P

P1

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Quote reached in rapid  at the end of  the cycle

INI –  Initial Drilling Quote [mm]

IND – Drilling  Increment [mm]

TIM – Dwell time [sec]

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Quote reached in rapid  at the end of  the cycle

INI –     Initial Drilling quote [mm]

IND –   Drilling  Increment  [mm]

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Quote reached in rapid at the beginning of cycle

RAL  -  Return  Quote reached at rapid

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Return  Quote reached at rapid  with spindle stopped.

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Return  Quote reached at rapid  with spindle stopped, oriented and disengaged.

DAX -  Incremental disengagement  movement along X

DAY -  Incremental disengagement  movement along  Y

Parameters description:

ENT - Depth  quote reached  at working feed

RAP - Quote reached in rapid at the beginning of cycle

RAL - Return  Quote reached at rapid

TIM - Dwell [sec]  to start  working movement between ENT and RAP.

or  +

G1 X100Y100 SM5

X200 Y0

…

G2 I40 J25 R20 RA-10

G1 RC30 X80  Y100

….

……

G1 RC30 RA10

G2 I40 J25 R20

……

or an arc and a line

….

G2 I30  J20  R15 RA20

G2 I70 J25 R20

…..

G1 X100Y100 RA4

X200 Y0

Syntax:

L<TRACYL> <DIA=…>

where

DIA = diameter of the Cylinder where the working is applied.

or  +

Parameters descriptions:

DTX, DTY, DTZ, ANR and %NPR have the same meaning  of the homonymous variables used in the matrix TRANS and ROT..

XCE, YCE are instead the co-ordinates of the point from which the profile is rotated the first time.

or  +

or  +

+

or  +

Parameters description:

X.. Y.. -  Absolute coordinates, on the Contouring Plane, of the measurement starting point (P1/P2).

Concerning  ENT, RAL, RAP, MIS and F see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Z.. -  Absolute coordinates on the Contouring Plane of the measure starting point (P).

DAX – Distance between the starting point  and the contact surface of the probe . Distance given along the axis where canned cycles will be applied (Z in case of  issuing of a <CFF=CFZ> instruction).

Concerning  MIS and TYP  see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates on the Contouring Plane of the center of the arc to be measured (P).

DIA – Diameter of the arc to be measured.

AIN – Angle related  to the first measurement  movement. It is defined with reference to the first axis of the Contouring Plane. If positive  the sense of rotation will be anti clockwise, if negative  clockwise.

ANA – Angular increment to define the second and the  third movement .

Concerning F, RAL, RAP, ENT, LTZ, STZ, ROT, MIS and TYP  see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates on the Contouring Plane of the measure starting point (P).

DAX – Distance between the two measurement points in the direction of the first axis of the Contouring Plane (X in case of C.P. definition through the instruction G16XYZ+).

DAY – Distance between ENT quote and the surface part (considering the part perfectly  aligned).

AXS – Rotative Axis of which must be corrected the origin Insert <AXS=CFA> if the axis is A, <AXS=CFB> if is B , etc.

Concerning F, RAL, RAP, ENT, LTZ, STZ, MIS and TYP  see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates on the Contouring Plane of the center of the arc  to be measured (P).

DIA – Diameter of the arc to be measured.

AIN – Angle related  to the first measurement  movement. It is defined with reference to the first axis of the Contouring Plane. If positive  the sense of rotation will be anti clockwise, if negative  clockwise.

ANA – Angular increment to define the second an the third movement .

Concerning F, RAL, RAP, ENT, LTZ, STZ, ROT, MIS and TYP  see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates on the Contouring Plane of the center of the hole to be measured (P).

DIA – Diameter of the hole to be measured.

AIN – Angle related  to the first measurement  movement. It is defined with reference to the first axis of the Contouring Plane. If positive  the sense of rotation will be anti clockwise, if negative  clockwise.

Concerning F, RAL, RAP, ENT, LTZ, STZ, ROT, MIS and TYP  see, for details , “Preparatory Parameters & Instructions”.

Parameters description:

Same as for G202 Measurement Cycle (see).

Parameters description:

X.. Y.. -  Absolute coordinates of the starting point of the measuring cycle, must stay on the programmed contouring plane (P).

MIS      -  Definition of the type of measurement to be executed

TYP     -   Definition of the type of correction and of the Responsible factor to which the measured error has to be attributed.

Concerning F, RAL, RAP, ENT, LTZ, STZ, ROT  see, for details, “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates of the starting point of the measuring cycle, selected on the programmed contouring plane (P).

MIS - Definition of the type of measurement to be executed

TYP -  Definition of the type of correction and of the Responsible factor to which the measured error has to be attributed.

Concerning  F, RAL, RAP ed  ENT see, for details , “Preparatory Parameters & Instructions”.

Parameters description:

X.. Y.. -  Absolute coordinates on the Contouring Plane of the center of the cylinder to be measured (P).

DIA – Diameter of the cylinder to be measured.

AIN – Angle related  to the first measurement  movement. It is defined with reference to the first axis of the Contouring Plane. If positive  the sense of rotation will be anti clockwise, if negative  clockwise.

Concerning F, RAL, RAP, ENT, LTZ, STZ, ROT, MIS and TYP see, for details , “Preparatory Parameters & Instructions”.

Section 1

Y

Parameters description:

XAT /YAT   – Point from which  the tool move to attach the “Flat”  profile. If not defined the movement will start from the position reached before the  G738 calling.

%RAC - Type of link between the elements of the flat profile in function of the section:

%RAC=1  ( Variable radius link (default )

%RAC=2  (  Fixed radius link

3D Surface obtained

Parameters description:

XAT /YAT   – Point from which  the tool move to attach the first profile. If not defined the movement will start from the position reached before the  G728 calling.

QIN  - Quote of the first involved profile.

QFO -  Quote of the second involved profile.

Graphic meaning of %FON parameter

%FON=0

%FON=1

PIN

RIN

QFI

QIN

Z

PIN

RIN

QFI

QIN

Z

Parameters description:

I.. J..  – Co-ordinate f the Center of the Spiral

RIN  - Spiral Starting Radius

RFI  -  Spiral Final Radius

QIN – Spiral Starting Quote

QFI – Spiral Final Quote

DPA – Spiral Pitch

Correspondent Graphical Representation

Parameters description:

QFO - Pocket bottom quote

QIN - Pocket top quote

PPA - Pass depth

QPO - Rapid Safe Co-ordinate (default=DQS)

APA - Pass inclination angle (default 0°)

DQS - Safe quote reached at the begin  of every step (default QIN + 2 mm).

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Approach quote reached in rapid

RAL  -  Extraction quote reached in rapid

Differences between standard FORMAT:

%NRG =0

PXR and PYR distances without meaning

Parameters description:

X.. Y.. -  Coordinate of the first  application point of cycle/macro

%NHL – Number of columns

%NRG – Number of rows

PXL – Distance, along X, between to contiguous points on the same row

PYL – Distance , along Y, between to contiguous points on the same row

PXR - Distance, along X, between to contiguous points on the same column

PYR - Distance, along Y, between to contiguous points on the same column

The Macro G179  uses the same parameters of the Macro G189. The only difference is:

ANL  - Defines the angle [°] applied on depth increases  starting from attach point.

The Macro G175  uses the same parameters of the Macro G185. The only difference is:

ANL - Defines the angle [°] applied on depth increases  starting from attach point.

The Macro G190  uses the same parameters of the Macros G179 and G189. The only difference are:

RGS - Represents the maximum height of the peak which must remain between  two contiguous passes expressed in micron. If ASF=0, RGS becomes the increase in depth (therefore similar to the parameter INI of G179-G189). In this case it  must be expressed in mm.

RUT-  It has different meaning  in base to the tool shape. In the case of  Spherical tools it is the tool  radius.

In  case of a Toric tool it is the radius of the blade (for a  Cylindrical tool it must be however set  not 0 but very small  (usually 0.1mm).

SME – Stock allowance present on the work .piece.

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Approach quote reached in rapid

RAL  -  Extraction quote reached in rapid

DIA –   Hole  diameter  [mm].

ROT – Sense of rotation

ROT=2 Clockwise  ROT=3 Anti clockwise

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Approach quote reached in rapid

RAL  -  Extraction quote reached in rapid

ANA –   Opening angle  of the Pocket . It is positive

if measured  in an anti-clockwise direction , while  negative if  measured in clockwise direction (in both cases starting from the initial point P)

ROT – Sense of rotation

ROT=2 Clockwise  ROT=3 Anti clockwise

The Macro G186 uses the same parameters of the Macros G175 and G185. The only differences are:

RGS  - It represents the maximum height of the peak which must remain between  two contiguous passes expressed in micron.  If ASF=0, RGS becomes the increase in depth (therefore similar to the parameter INI of G175-G185). In this case it  must be expressed in mm.

RUT-  It has different meaning  in base to the used  tool shape. In the case of  Spherical tools it is the tool  radius.

In  case of  a Toroidal  tools it is the radius of the blade (for a  Cylindrical tool it must be however set  different from  0 also if  very small  (usually 0.1mm).

Parameters description:

ENT - Depth  quote reached  at working feed

RAP - Approach quote reached in rapid

RAL - Extraction quote reached in rapid

ANA - Represents the inclination of the pocket respect the X axis. It is positive if measured  in an anti-clockwise direction, negative if in clockwise direction.

ROT – Sense of rotation

ROT=2 Clockwise  ROT=3 Anti clockwise

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Approach quote reached in rapid

RAL  -  Extraction quote reached in rapid  at the end of  the cycle

DIA –   Cylinder  diameter  [mm].

ROT – Sense of rotation

ROT=2 Clockwise  ROT=3 Anti clockwise

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  - Approach quote reached in rapid

RAL  -  Extraction quote reached in rapid  at the end of  the cycle

DIA – Hole diameter  [mm].

ROT – Sense of rotation

ROT = 2 Clockwise  ROT=3 Anti clockwise

A matrix can always be represented by three equations in the form:

Zb = a11*Zl	+ a12*Xl + a13*Ql + a14

Yb = a21*Zl	+ a22*Xl + a23*Ql + a24

Zb = a31*Zl	+ a32*Xl + a33*Ql + a34

+

Note :

The K  code will identify the solution characterized by the arc that    subtend the bigger angle.

G24 X max Y max Z max

G23   X min Y min  Z min

Volume Working Limit

Z

Y

X

Y

G19

G17

G18

G03

G03

G03

X

Z

P1

J

Y

e

a

Ypole

X

G42

G41

P4

P3

P2

50    90      137.5         225     283.33  341.66  550         610          X

Y

350

343

275

260

240

200

150

100

%

N0   G90 T6 M6 G16XYZ+

N10  G0 X90 Y240 S...  F....                   { Pin}

N20  Z-30 M13

N30  G42 X50 Y350     	                      { P1}

N40  G2 I137.5  J275 X225 Y200           { P2}

N50  G3 I283.33 J150 X341.66 Y100     { P3}

N60  G1 X550 Y 343                                { P4}

N70  G0 G40 X610 Y260                         { Pend}

.....

G41 / G42 K

Element1

Element2

……..

G41 / G42 Element1

Element2

Element2

Element1

Y

X

Element n

G46 K  X.. Y..

Parameters description:

ENT  - Depth  quote reached  at working feed

RAP  -  Quote reached in rapid at the beginning of cycle

RAL  -  Quote reached in rapid  at the end of  the cycle

Modality

Angle from which Feed is reduced

Angle

3

2

1

Angle where movement is stopped

movimento

SGL is respected?

CSGL is respected?

G64

No

AG64 (90°)

No

No

G66

No

AG66 (60°)

Yes

Yes

G60

ANGI (3°)

ANGF(30°)

Yes

Yes

G67 Function  Smoothing effect            (

Angle

3

2

1

(      G67 Function Filtering effect